## Slide 1
DEEPGRID SEMI · D100 · DRONE SOC
A failsafe that does not trust its flight computer.
Flight control, visual-inertial navigation and a hardware failsafe island with its own power, clock and path to the ESCs.
30 Hz
SIX-DOF POSE, NO GPS
1080p60
MIPI CSI-2 CAMERA, 2 LANES
200 MHz
130 NM CONTROL DIE
PRE-SILICON ARCHITECTURE
Every figure in this deck is a design target. An FPGA prototype validates the design; no D100 silicon has been fabricated or measured.
DEEPGRID SEMI · D100 ARCHITECTURE · OCTOBER 2026
Notes: D100 is the drone SoC in the DeepGrid portfolio. Headline and lede: D100 product page ("A drone SoC whose failsafe does not trust its own flight computer"). Figures: product page specs (hardware VIO, six-DoF EKF at 30 Hz; MIPI CSI-2, two lanes, to 1080p60, with ISP; 130 nm CMOS at 200 MHz). Status: D100 Architecture Guide header ("An FPGA prototype validates the design; no D100 silicon has been fabricated or measured") and the portfolio status record (the drone position engine runs as circuit code on an Artix-7 FPGA). Status: pre-silicon. No D100 silicon has been fabricated or measured; an FPGA prototype validates the design. Every figure is an architecture target from the D100 product page or the D100 Architecture Guide, not a measurement.

## Slide 2
01 · WHAT IT IS
One SoC flies, navigates and recovers the airframe
Three jobs on one 130 nm die at 200 MHz, with an optional accelerator die joining the package later.
DEEPGRID SEMI · D100 DRONE SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
02
Flies the airframe
Two DGridRiscV cores run the PX4 or ArduPilot loop in hard real time. IMU, magnetometer and barometer come in; motor commands leave as PWM or DShot to the ESCs.
Navigates without GPS
A hardware visual-inertial engine takes a MIPI CSI-2 camera through an ISP and feature extraction, and a Kalman pose engine fuses it with the IMU into a six-DoF pose at 30 Hz.
Recovers on its own
A failsafe island with its own power and clock watches the radio link and the flight computer from outside, and can take the motors through an independent path to the ESCs.
PHASE 2 · OPTIONAL
A 10 TOPS INT8/INT4 accelerator with 2 MB of on-chip memory adds object detection on a separate 28 nm die in the same package. Flight control and the failsafe never depend on it.
The failsafe island watches the link and the flight computer from outside; it does not run as a task inside the flight stack.
Notes: Source: D100 product page, lede, blocks and block note; D100 Architecture Guide, "What is D100?". Flight control: two DGridRiscV cores for PX4 or ArduPilot loops, IMU, magnetometer, barometer, ESC out (PWM, DShot). Visual-inertial odometry: MIPI CSI-2 camera input and ISP, feature extraction, Kalman pose engine at 30 Hz. AI accelerator (phase 2): 10 TOPS INT8/INT4 array, 2 MB on-chip memory, object detection. Failsafe island: link monitor, safe-state machine, independent path to the ESCs. The guide calls the accelerator "variant 2" and "about 10 TOPS class"; the product page wording is used. Status: pre-silicon. No D100 silicon has been fabricated or measured; an FPGA prototype validates the design. Every figure is an architecture target from the D100 product page or the D100 Architecture Guide, not a measurement.

## Slide 3
02 · WHY IT NEEDS ITS OWN SILICON
Three requirements force the island and die split
Each requirement of a drone flight computer has a direct consequence for how the silicon is built.
DEEPGRID SEMI · D100 DRONE SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
03
REQUIREMENT
CONSEQUENCE FOR THE SILICON
Recover
Recovery must work when the flight software has failed.
A separate safe-state machine and link monitor in their own power and clock domain, wired directly to the ESCs.
No GPS
Navigation without GPS.
A hardware visual-inertial engine running a six-degree-of-freedom Kalman filter at 30 Hz.
Vision
Vision AI needs dense logic that 130 nm cannot supply.
Control and failsafe on 130 nm; an optional accelerator on a 28 nm die joins in the package later.
Together these set the part: a 130 nm CMOS die at 200 MHz for control and failsafe, and a proposed 28 nm accelerator die in the same package.
Notes: Source: D100 product page, physics (requirement and consequence, three pairs), quoted. Process: product page specs, "130 nm CMOS at 200 MHz; proposed 28 nm accelerator die in the same package". D100 Architecture Guide, AI accelerator section: "vision AI needs dense logic that 130 nm cannot supply, so the accelerator is a 28 nm die that joins the same package in a later wave". Status: pre-silicon. No D100 silicon has been fabricated or measured; an FPGA prototype validates the design. Every figure is an architecture target from the D100 product page or the D100 Architecture Guide, not a measurement.

## Slide 4
03 · SYSTEM ARCHITECTURE
Five groups on one crossbar; the island sits apart
Redrawn from Technical Annex v3, sheet 11. Markers 1 to 4 are normal flight; 5 and F are a failsafe trip.
DEEPGRID SEMI · D100 DRONE SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
04
External: cameras · IMU, magnetometer, barometer · RC receiver and telemetry radio
FLIGHT CONTROL · HARD REAL-TIME
DGridRiscV × 2
RV32IM_Zicsr · FC core + NAV core · PX4 or ArduPilot
IMU / MAG / BARO
SPI × 3 · 8 kHz
ESC OUT
PWM or DShot · DShot600 × 8
RC + telemetry
SBUS · CRSF · MAVLink over UART
VISUAL-INERTIAL ODOMETRY
MIPI CSI-2
2 lanes · to 1080p60
ISP
rectify + lens shading
Feature
FAST + BRIEF · ~2k points
Pose engine
EKF · IMU pre-integration · sliding-window BA · six-DoF pose at 30 Hz
AI · PHASE 2 · OPTIONAL 28 NM DIE
NPU
10 TOPS INT8/INT4 · 2 MB SRAM · DMA
Detection
object detection; segmentation for obstacle avoidance
AXI4 crossbar · 128-bit · 200 MHz
FAILSAFE ISLAND · OWN POWER, CLOCK
Link monitor
radio loss · GPS denial · IMU fault · in hardware
Safe-state FSM
return to home or land
Independent path
direct to the ESCs · bypasses FC, VIO and AI
PLATFORM
LPDDR4
2 GB · 32-bit
eMMC / NAND
logging
PMU
5 power domains
SEC
secure boot
Gigabit Ethernet / USB 3
payload + ground link
CAN-FD × 2 · SPI · I²C
gimbal, payload
JTAG
debug
independent of the mission stack
External: ESCs and motors
Sensors and RC reach the flight cores.
Camera frames run ISP, features, pose.
The 30 Hz pose reaches the flight loop.
Motor commands leave on ESC OUT.
Link monitor trips the safe-state FSM.
The island takes the ESCs directly.
1
2
3
4
5
F
1
2
3
4
5
F
Notes: Source: D100 native diagram specification and D100 Architecture Guide, "Architecture Overview" and the five component sections; figure redrawn from Technical Annex v3, sheet 11 (Fig 3), as native editable shapes. Five groups: flight control, visual-inertial odometry and the phase-2 AI die above a 128-bit AXI4 crossbar at 200 MHz; the failsafe island and the platform below. The failsafe island has isolated power and clock and its own path to the ESCs; the guide states the failsafe path is independent of the mission stack. Markers follow the guide's Key Data Flows: 1 sensors and the RC link reach the flight cores; 2 the cameras run through the ISP and feature extractor to the pose engine; 3 the 30 Hz pose reaches the flight loop over the crossbar; 4 motor commands leave on ESC OUT; 5 the link monitor trips the safe-state machine on RC loss, GPS loss or an IMU fault; F the independent path takes the ESCs directly, bypassing the flight cores, the odometry and the AI. Values follow the product page where sources differ: the annex sheet shows the camera as a stereo pair at 720p60; the product page gives two lanes, up to 1080p60. Status: pre-silicon. No D100 silicon has been fabricated or measured; an FPGA prototype validates the design. Every figure is an architecture target from the D100 product page or the D100 Architecture Guide, not a measurement.

## Slide 5
04 · COMPONENTS
Four blocks fly the craft; one can overrule them
Flight control, odometry and the phase-2 AI share the crossbar; the failsafe island acts from outside it.
DEEPGRID SEMI · D100 DRONE SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
05
Flight control
Two DGridRiscV cores, RV32IM_Zicsr, one for flight control and one for navigation, run PX4 or ArduPilot. IMU, magnetometer and barometer on three SPI links at 8 kHz; DShot600 on eight channels; SBUS, CRSF and MAVLink over UART.
Visual-inertial odometry
Two-lane MIPI CSI-2 to 1080p60, an ISP for rectification and lens shading, FAST corners with BRIEF descriptors at about 2k points per frame, and an EKF pose engine at 30 Hz. Geometry, not learned perception.
Failsafe island
A hardware link monitor sees radio loss, GPS denial or an IMU fault and trips a safe-state machine: return to home or land. An independent path drives the ESCs, on isolated power and clock.
AI accelerator, phase 2
An optional 10 TOPS INT8/INT4 array with 2 MB of SRAM and DMA, for object detection. It sits on a 28 nm die in the same package; flight and failsafe do not depend on it.
Platform: LPDDR4 (2 GB, 32-bit), eMMC or NAND for logging, a PMU with five power domains, secure boot, Gigabit Ethernet and USB 3, CAN-FD × 2, SPI and I²C for gimbal and payload, and JTAG.
Notes: Source: D100 Architecture Guide, component sections (Flight control, Visual-inertial odometry, AI accelerator, Failsafe island, Platform); D100 product page blocks. The guide states the odometry is geometry, not learned perception, so it needs no trained model to hold a pose. The product page names the link monitor inputs as radio loss and GPS denial; the guide adds IMU fault. The product page lists LPDDR4 as 32-bit; the 2 GB capacity is from the guide. Status: pre-silicon. No D100 silicon has been fabricated or measured; an FPGA prototype validates the design. Every figure is an architecture target from the D100 product page or the D100 Architecture Guide, not a measurement.

## Slide 6
05 · DESIGN DECISIONS
Each design choice buys independence at a cost
What each architectural choice buys, and the engineering condition it creates for evaluation.
DEEPGRID SEMI · D100 DRONE SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
06
DECISION
WHAT IT BUYS
WHAT IT ASKS OF THE DESIGN
Failsafe as separate hardware, own power and clock
Recovery that still works when the flight stack hangs
Define what the island must see to act, and prove the trip path without the flight cores
Navigation as geometry: EKF with FAST and BRIEF
A pose without GPS and without a trained model
Drift per kilometre is unmeasured; the evaluation must test it under GPS denial
Control and failsafe on 130 nm, AI on a 28 nm die
Flight functions never depend on the accelerator
The 28 nm die is proposed for phase 2; detection waits for it
One 128-bit AXI4 crossbar at a fixed 200 MHz
One fabric for cores, pose engine, NPU and memory
Timing is closed on an FPGA at 81.25 MHz only; 200 MHz on an open process is open
One package: 15 × 15 mm BGA, flip-chip 28 nm die, not UCIe
Dies join over substrate SPI, UART and GPIO
Heat from the camera pipeline and flight loops must leave a closed fuselage at +55 °C
Rows 1, 2, 4 and 5 are the four questions on slide 9. None is answered yet; each needs simulation, layout or silicon data.
Notes: Source: D100 product page physics, specs, reconcile and questions; D100 Architecture Guide sections "Failsafe island" (why it exists), "Visual-inertial odometry" (why it is geometry), "AI accelerator" (why a separate die), "Prototype and product" (Artix-7 FPGA at 81.25 MHz, validation only; 130 nm ASIC, SkyWater SKY130 / IHP SG13G2 open PDK, 200 MHz fixed) and "Package" (SiP sheet: four-layer organic substrate, 15 × 15 mm BGA, flip-chip 28 nm compute die, die-to-die SPI, UART and GPIO over the substrate, deliberately not UCIe). FPGA timing closure is a prototype milestone, not a measurement of the ASIC. The third column restates the product page questions. Status: pre-silicon. No D100 silicon has been fabricated or measured; an FPGA prototype validates the design. Every figure is an architecture target from the D100 product page or the D100 Architecture Guide, not a measurement.

## Slide 7
06 · KEY DATA FLOW
Normal flight takes four steps; a trip takes three
Numbers match slide 4. The flight loop uses the crossbar; the trip uses the island and its own path.
DEEPGRID SEMI · D100 DRONE SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
07
Normal flight
Sense
IMU, magnetometer, barometer and the RC link reach the flight cores.
See
Camera frames run through the ISP and the feature extractor to the pose engine.
Locate
The 30 Hz six-DoF pose reaches the flight loop over the crossbar.
Command
The flight loop sends motor commands on ESC OUT.
1
2
3
4
Failsafe trip
Detect
The link monitor sees radio loss, GPS denial or an IMU fault, in hardware.
Decide
It trips the safe-state machine, which selects return to home or land.
Take over
The independent path drives the ESCs directly, bypassing the flight cores, odometry and AI.
5a
5b
F
The trip path bypasses the flight cores, odometry and AI, so a hung flight stack is not in its way.
Notes: Source: D100 Architecture Guide, "Key Data Flows": Normal flight (four steps) and A failsafe trip (three steps), restated; marker numbering follows the native diagram specification (1 to 4 normal flight, 5 the link monitor, F the independent path). Product page block note: "The failsafe island watches the link and the flight computer from outside and can take the motors on its own." The guide names RC loss and GPS loss; the product page says radio loss and GPS denial, used here. Status: pre-silicon. No D100 silicon has been fabricated or measured; an FPGA prototype validates the design. Every figure is an architecture target from the D100 product page or the D100 Architecture Guide, not a measurement.

## Slide 8
07 · ARCHITECTURE TARGETS
Seven figures, all architecture targets
Architecture targets from the D100 product page. No figure below comes from measured silicon.
DEEPGRID SEMI · D100 DRONE SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
08
PARAMETER
ARCHITECTURE TARGET
STATUS
Process
130 nm CMOS at 200 MHz; proposed 28 nm accelerator die in the same package
Target
Flight control
Dual DGridRiscV, hard real-time PX4 or ArduPilot
Target
Navigation
Hardware VIO, six-DoF EKF at 30 Hz
Target
Vision input
MIPI CSI-2, two lanes, to 1080p60, with ISP
Target
AI (phase 2)
Optional 10 TOPS INT8/INT4, 2 MB SRAM
Target
Failsafe
Independent watchdog and safe-state machine, isolated power and clock, direct ESC link
Target
Memory
LPDDR4 32-bit, eMMC or NAND
Target
Designed toward
DGCA type certification path · STANAG 4586 · MIL-STD-810H. Not held; no certificate exists.
Not established by this architecture
Jamming immunity · certified flight safety · a measured drift figure (open question) · an awarded contract.
Notes: Source: D100 product page specs (seven rows, quoted) and designedToward list; product page reconcile: "The failsafe architecture does not establish jamming immunity or certified flight safety." D100 Architecture Guide, "What the architecture does not establish": jamming immunity (the GPS-denied use case is a design intent, not a tested result), certified flight safety (a DGCA type-certification path is named; no certificate exists), navigation accuracy (no drift figure has been measured; the product page lists it as an open question). The guide header also states the failsafe architecture does not establish an awarded silicon contract. The guide adds detail the product page omits: LPDDR4 2 GB; NPU about 10 TOPS class. Status: pre-silicon. No D100 silicon has been fabricated or measured; an FPGA prototype validates the design. Every figure is an architecture target from the D100 product page or the D100 Architecture Guide, not a measurement.

## Slide 9
08 · EVALUATION
Four questions decide if D100 fits your airframe
The engineering questions the D100 architecture sheet asks of itself, for your evaluation.
DEEPGRID SEMI · D100 DRONE SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
09
1 · Hardware failsafe
Why is the safe-state logic separate hardware rather than a task in the flight stack, and what does it need to see to act?
2 · GPS-denied drift
Can the 30 Hz pose engine hold under 1% drift per kilometre under jamming, without learned weights?
3 · Thermal envelope
How is heat removed in a closed fuselage at +55 °C with the camera pipeline and flight loops running?
4 · From FPGA to silicon
Which timing paths in the 128-bit crossbar had to change to close at 200 MHz on an open process?
WHAT THE SOURCES SAY TODAY
1
The guide gives the reason: recovery must work when the flight software is what failed.
2
No drift figure has been measured; the guide lists it as an open question.
3
Neither the guide nor the annex sheet gives a thermal design yet.
4
Timing has closed only on the Artix-7 FPGA prototype at 81.25 MHz.
Notes: Question 2 asks for a target, not a result: no drift figure has been measured. Ask for each answer as simulation, layout or test data, and note which kind it is. What the sources say today: D100 Architecture Guide, "Failsafe island" (why it exists), "What the architecture does not establish" (navigation accuracy), "Prototype and product" (Artix-7 FPGA at 81.25 MHz, validation only); the guide and annex sheet 11 carry no thermal design. Source: D100 product page, questions (four, quoted verbatim): hardware failsafe, GPS-denied drift, thermal envelope, from FPGA to silicon. The figures in them (30 Hz, 1% per kilometre, +55 °C, 128-bit, 200 MHz) are from the same record. The 1% per kilometre figure is the question's threshold, not a claimed result: the D100 Architecture Guide states no drift figure has been measured. Status: pre-silicon. No D100 silicon has been fabricated or measured; an FPGA prototype validates the design. Every figure is an architecture target from the D100 product page or the D100 Architecture Guide, not a measurement.

## Slide 10
09 · NEXT STEP
Test the trip path and the pose engine first
A failsafe that acts without the flight computer is worth testing on the four questions before design-in.
DEEPGRID SEMI · D100 DRONE SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
10
NEXT STEP
Scope an evaluation of the trip path and the pose engine.
Request the D100 architecture guide and Technical Annex v3, sheet 11. Bring your airframe, link and payload needs and your thermal envelope.
CONTACT
group@deepgrid.in
Recovery is hardware
Own power, clock and ESC path; it acts without the flight computer.
Navigation needs no GPS
Camera and IMU fuse into a six-DoF pose at 30 Hz, without GPS.
AI is optional and separate
10 TOPS on a 28 nm die in phase 2; flight never depends on it.
Pre-silicon, stated plainly
Every figure is a target. Jamming immunity, certified flight safety and drift are not established.
Notes: Summary of slides 1 to 9. Sources: D100 product page (headline, lede, physics, specs, designedToward, reconcile, questions); D100 Architecture Guide (including "What the architecture does not establish"); Technical Annex v3, sheet 11 and the SiP sheet; portfolio status record for D100 (FPGA-validated: the drone position engine runs as circuit code on an Artix-7). Contact address from the DeepGrid site contact page. Status: pre-silicon. No D100 silicon has been fabricated or measured; an FPGA prototype validates the design. Every figure is an architecture target from the D100 product page or the D100 Architecture Guide, not a measurement.