## Slide 1
DEEPGRID SEMI · DG32-LITE · SEPTEMBER 2026
Lockstep safety on an entry-level motor chip
Dual-core lockstep RISC-V motor-control SoC · 130 nm CMOS · first silicon on the September 2026 multi-project shuttle
QFN-64 · 9 × 9 MM · ILLUSTRATIVE
2 × RV32IM
CORES IN HARDWARE LOCKSTEP
~100 kHz
CURRENT LOOP, SIMULATED
44
SIGNAL PINS IN QFN-64
39 cycles
FAULT TO LATCH, SIMULATED
Pre-silicon: figures are design values verified in simulation and static timing unless marked measured.
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
01
Notes: DG32-LITE is Deepgrid Semi's motor-control chip, and it makes one argument: hardware lockstep safety no longer needs an automotive-class microcontroller. Two RISC-V cores check each other on every write, inside a nine-by-nine millimetre package. First silicon rides the September 2026 multi-project shuttle, so every figure you will see is a design value, verified in simulation and timing analysis.

## Slide 2
02 · EXECUTIVE SUMMARY
One chip carries the MCU and its safety monitor
DG32-LITE in one slide: what it is, how it protects the drive, and what the control loop costs
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
02
THE ANSWER
One 130 nm chip carries the microcontroller, the motor-control peripherals and a hardware safety monitor.
Two RISC-V cores run in lockstep and must agree on every committed store. The expensive steps of field-oriented control run in dedicated blocks, so the cost of one loop is fixed and known.
First silicon: September 2026 multi-project shuttle
2 × RV32IM
LOCKSTEP CORES
CHECKER runs the same instructions two cycles behind MAIN
~100 kHz
CURRENT LOOP
Simulated: ~5 µs acquisition plus ~5 µs compute
39 cycles
FAULT TO LATCH
Simulated inject-to-latch latency, then FAULT_N drives low
~0.43 W
POWER AT 50 MHZ
Tool estimate at 25 °C and 1.8 V, not measured
Sources: DG32-LITE block architecture (loop, fault latency); investor block diagram; LITE preliminary datasheet (power).
Notes: Here is the whole case in brief. DG32-LITE puts a microcontroller, its motor peripherals and its own safety monitor, built in hardware, into one one-hundred-thirty-nanometre part. The two cores check each other on every stored write. In simulation the current loop reaches about one hundred kilohertz, and a disagreement is latched within thirty-nine cycles, driving a pin that can shut the power bridge off.

## Slide 3
03 · WHY LOCKSTEP
A silent CPU fault can destroy a power bridge
A motor drive turns every computed value into a gate command within one PWM period
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
03
CPU fault
A datapath error changes a computed value
Wrong PWM edge
The bad value becomes a gate command
Shoot-through
Both switches of one bridge leg conduct
Bridge damage
The power stage fails, not only the code
Today’s safeguards
Independent and window watchdogs, brown-out reset and periodic software self-test. The checks run between faults, not during them.
Where lockstep lives
Automotive microcontrollers such as Infineon AURIX, NXP S32K and TI Hercules compare two cores in hardware.
What DG32-LITE changes
Two RISC-V cores compare every committed store at a fixed latency, on an entry-level motor-control chip.
Sources: DG32-LITE block architecture §4.1; investor block diagram p2 (STM32G0 column from public datasheet values).
Notes: Why build it this way? A motor drive switches power transistors thousands of times a second. If the CPU silently computes a wrong value, it writes a wrong PWM edge, and a wrong edge can short a bridge leg. Entry-level motor MCUs catch faults with watchdogs and periodic software self-test. Hardware lockstep has lived in automotive parts such as AURIX, S32K and Hercules.

## Slide 4
04 · ARCHITECTURE
Six block groups share one deterministic bus
DG32-LITE on one 50 MHz clock domain: safety, memory and supervision above the bus; the drive below
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
04
Safety core
MAIN + CHECKER cores
Lockstep comparator
Fault latch → FAULT_N
Memory & boot
Boot ROM, 64 KB
SRAM, 32 KB dual-port
QSPI controller · DMA
Supervision
Windowed watchdog
Supply supervisor
Interrupts, 16 sources
On-chip bus · two masters · deterministic · bus error, never a hang
Motor drive
3-phase PWM + brake
DShot × 4
Timers × 2
Sensing & math
SAR ADC, 8-bit
Encoder + Hall
CORDIC
Connectivity & test
UART × 2 · SPI · I²C
GPIO, atomic set/clear
JTAG + scan chains
DG32-LITE block groups · 130 nm CMOS · pre-silicon design
1
Two masters
The CPU and a DMA share the bus; the CPU always has priority.
2
Deterministic latency
One outstanding request at a time keeps timing predictable.
3
Faults contained
Unmapped or disabled addresses return a bus error instead of hanging.
4
Register slaves
Every peripheral is a 32-bit register block on the same bus.
Sources: DG32-LITE investor block diagram p1; tape-in block diagram; block architecture §3.
Notes: The architecture is six groups of blocks around a single bus. The safety core, the memory and the supervisors sit on one side of it; the motor drive, sensing and math, and connectivity and test sit on the other. Only the CPU and a DMA can start a transfer, and every transfer takes a predictable time. Because the chip has no debugger halt, a bad address returns an error rather than freezing it.

## Slide 5
05 · DESIGN PREMISES
Four hard constraints shaped every block
Each constraint is a finding from bringing up the hardened design, and each one sets a block’s shape
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
05
CONSTRAINT
WHAT IT MEANS
WHAT THE DESIGN DOES
No debugger halt on the die
Nothing outside the chip can stop or inspect a hung CPU
Bad accesses return a bus error; blank flash starts a UART monitor
Lockstep core fmax ~55–62 MHz
The core is the slowest block; peripherals exceed 90 MHz
The whole die runs one 50 MHz clock domain
CPU costs ~8 cycles per instruction
Control math in plain C is slow and variable
Sampling, transforms and PWM edges move into hardware
Memory macros have no spare bits
The 32-bit SRAM macros leave no room for parity or ECC
The chip ships without ECC and states it plainly
Why the third constraint matters most
Every step that would dominate a control loop on this core became a dedicated block.
Source: DG32-LITE block architecture §2, design premises. fmax is post-route on the hardened design.
Notes: Every design choice traces back to a limit found while hardening the chip. Nothing outside can halt the CPU, so nothing is allowed to hang. The lockstep core tops out between fifty-five and sixty-two megahertz, so the entire die is clocked at fifty. Each instruction costs about eight clock cycles, too slow for the loop, so the loop moved into hardware. And with no spare memory bits, the chip goes out without error correction, stated plainly.

## Slide 6
06 · SAFETY CORE
Two cores must agree on every committed store
The fault path runs from a datapath error to a hardware trip without firmware in the loop
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
06
MAIN core
Runs the application
CHECKER core
Same inputs, two cycles behind
Comparator
Checks every committed store
Fault latch
Holds the first cause
FAULT_N pin
Trips the gate driver
Fault injection
A locked register fires the fault path on purpose, the only way to prove it works on real silicon. Inject to latch: 39 cycles, simulated.
Windowed watchdog
A kick that arrives too early or too late both fault, so it catches runaway code as well as a hang. Firmware arms it after boot.
Supply supervision
Two supply-good inputs are deglitched and drive reset sequencing. Status and fault counts stay readable by firmware.
Interrupts and bus responses reach both cores identically, so firmware can branch on peripheral reads without the cores diverging.
Sources: DG32-LITE block architecture §4.1, §4.4–4.5; tape-in block diagram (checker timing, mirrored bus responses).
Notes: This is the safety core. MAIN runs the application. CHECKER runs the same instructions two cycles later, on the same inputs, and the comparator checks every committed store. On a mismatch, the first cause is latched and FAULT_N goes low. Route that pin to the gate-driver enable, and the bridge turns off in hardware, without waiting for firmware.

## Slide 7
07 · BOOT PATH
The chip boots itself, even with blank flash
No management core and no debugger: the mask ROM is the whole boot path
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
07
Power on
ROM prints the boot banner on UART0
Validate
Reads and checks the flash image header
Load
Copies the application into SRAM
Run
Jumps to SRAM; firmware enables interrupts
Blank flash still talks
With no valid image header, the ROM starts a UART monitor, so a bare board can be read, written and started without a debugger.
The trade-off
Code does not execute in place from flash. It runs from 32 KB of SRAM through a dedicated fetch port. Embedded flash is on the roadmap.
64 KB
BOOT ROM
Mask-programmed; starts the chip alone
32 KB
SRAM
16 dual-port macros: data and fetch
0
MANAGEMENT CORES
Nothing else is needed to start the chip
Sources: DG32-LITE preliminary datasheet §6 (clock, reset, boot); block architecture §4.2–4.3.
Notes: Reaching running code takes no helper processor or debugger. Hard-wired ROM logic greets the serial console, confirms the image in external flash is valid, loads it into SRAM and hands over control. A board with empty flash is not stranded either: the ROM drops into a serial monitor that can program and start it. The price is copying code at every boot, since nothing runs directly out of flash.

## Slide 8
08 · CONTROL SIGNAL CHAIN
The expensive steps of the loop run in hardware
One field-oriented-control tick, left to right; only step 4 runs on the CPU
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
08
1 Position
Encoder + Hall, edge timestamps
2 Sample
SAR ADC at PWM centre
3 Transform
CORDIC Clarke / Park
4 Regulate
Two PI loops on the CPU
5 Rotate back
CORDIC inverse Park
6 Drive
PWM, dead-time, brake
Only step 4 runs on the CPU
The core costs about 8 clock cycles per instruction, so it keeps the two PI regulators and nothing else. Every other step is a dedicated block with a fixed cost.
Why sample at the PWM centre
Centre-aligned PWM puts the sampling instant at the current-ripple null, so the ADC reads true phase current without analog filter delay.
≤ 2 cycles
HARDWARE BRAKE
All six gate outputs forced off
~200 kSa/s
SAR ADC
8-bit differential, on-die
53–58
CYCLES PER CORDIC OP
Fixed latency, simulated
Sources: DG32-LITE block architecture §4.12–4.16; LITE preliminary datasheet (brake, ADC, CORDIC).
Notes: Every expensive step of field-oriented control runs in a dedicated block. Encoder and Hall inputs give position, with edge timestamps. The PWM fires the ADC at the centre of each period, where ripple is lowest. The CORDIC computes the Park transforms, the CPU runs only the two PI regulators, and the PWM block applies the new duty cycles, with a hardware brake behind it.

## Slide 9
09 · LOOP COST
One current loop costs about 300 hardware cycles
Cycle costs per stage at the 50 MHz clock, where one cycle is 20 ns
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
09
STAGE
BLOCK
COST
Sample current
SAR ADC
177 cycles
Clarke / Park
CORDIC
53–58 per op
PI regulators
CPU, plain C
~8 per instruction
Inverse Park
CORDIC
53–58 per op
Update PWM
Shadow registers
next reload
Fault check
Comparator
continuous
~300 cycles
HARDWARE COST PER LOOP
ADC sample + two CORDIC operations + PWM write, the same at every loop rate
At 20 kHz
One period is 2,500 cycles. Hardware takes about 300 of them, 12%. The other ~2,200 cycles belong to firmware.
ONE 20 KHZ PERIOD, DRAWN TO SCALE (2,500 CYCLES)
HW 12%
Firmware budget: ~2,200 cycles, 88%
Source: DG32-LITE block architecture §5.1. Cycle costs measured in simulation. Derived: 300 ÷ 2,500 = 12%.
Notes: Here is what one loop costs. The current sample takes one hundred seventy-seven cycles. Each CORDIC operation takes fifty-three to fifty-eight. The regulators cost about eight cycles per instruction. Together the hardware part is about three hundred cycles, and it is the same at every loop rate. At twenty kilohertz, that is twelve percent of the period.

## Slide 10
10 · HEADROOM
At 20 kHz, 88% of each period is left for firmware
Budget = cycles per period minus the ~300 fixed hardware cycles
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
10
FIRMWARE BUDGET PER LOOP, CLOCK CYCLES AT 50 MHZ
~4,700
10 kHz
~2,200
20 kHz
~700
50 kHz
~200
100 kHz
10 kHz · ~4,700 cycles
Full current and speed loop, with an observer
20 kHz · ~2,200 cycles
FOC with field-weakening and an observer
50 kHz · ~700 cycles
Inner current loop only; tight regulators
100 kHz · ~200 cycles
Simulated ceiling: ~5 µs + ~5 µs
Source: DG32-LITE block architecture §5.2. 100 kHz row derived: 500 − 300 cycles.
Notes: So the question becomes how much firmware fits. At ten kilohertz there are about forty-seven hundred cycles left: enough for a full current and speed loop with an observer. At twenty kilohertz, twenty-two hundred, enough for field-weakening. At fifty kilohertz, seven hundred, an inner current loop only. The simulated ceiling is about one hundred kilohertz.

## Slide 11
11 · TIMING
Only the lockstep core limits the clock
Post-route maximum frequency per hardened block, MHz
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
11
GPIO
173.6
DShot
172.9
QSPI controller
171.6
PWM
167.8
Lockstep checker
123.6
CORDIC
95.5
Supervisor
91.1
Lockstep core
55–62
50 MHz die clock
50 MHz
DIE CLOCK
Set by the lockstep core at ~55–62 MHz, not by any peripheral
Peripherals have room
Every peripheral hardens above 90 MHz, more than 1.8× the die clock, so timing closure rests on one block.
Source: DG32-LITE block architecture §5.3, post-route. The lockstep-core bar is drawn at 55 MHz, the low end of its range.
Notes: Timing tells the same story. After place-and-route, the GPIO, DShot, QSPI and PWM blocks all run above one hundred sixty-five megahertz, and CORDIC and the supervisor above ninety. Only the lockstep core, at fifty-five to sixty-two megahertz, sets the clock. No peripheral is ever the timing wall.

## Slide 12
12 · PACKAGE
44 signals and a hardware trip in 9 × 9 mm
QFN-64 top to bottom: 44 signal pins, 20 supplies and grounds, one exposed ground paddle
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
12
FUNCTION
SIGNALS
PINS
Motor PWM
AH, AL, BH, BL, CH, CL + ADC trigger
7
Position sensing
Encoder A, B, Z · Hall A, B, C
6
Analog
SAR ADC VINP, VINN (0–1.8 V)
2
QSPI flash
Clock, 4 data, 2 chip selects
7
Serial
UART0 TX/RX · UART1 TX/RX
4
SPI
SCLK, MOSI, MISO, CSN
4
I²C
SCL, SDA (open-drain)
2
GPIO
GPIO0–2
3
Safety
FAULT_N · 2 × supply-good inputs
3
JTAG
TCK, TMS, TDI, TDO
4
Clock & reset
CLK, RST_N
2
9 × 9 mm
QFN-64 BODY
0.5 mm pitch, ground paddle
44
SIGNAL PINS
Plus 20 supplies and grounds
1.8 V
CORE SUPPLY
I/O pad ring at 3.3 V
Identical
DG32-2DOM PINOUT
The engine adds no pads
FAULT_N is the hardware trip
Route it to the gate-driver enable so a CPU disagreement turns the bridge off.
Sources: DG32-LITE preliminary datasheet §2–3, §5, §10; DG32-2DOM preliminary datasheet §2 (identical pinout).
Notes: All of it fits a nine-by-nine millimetre QFN with sixty-four pins: forty-four signals, and the rest power and ground. Seven pins drive the bridge, six read position, two carry the analog current input, and a single pin, FAULT_N, shuts the drive down in hardware. Because DG32-2DOM uses exactly this pinout, a board built for one takes either chip.

## Slide 13
13 · COMPUTE VARIANT
DG32-2DOM adds AI without slowing control
The same chip plus an INT8 attention engine on its own clock, in the same 64-pin footprint
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
13
50 MHz control domain
Lockstep CPU pair
Motor peripherals
Boot ROM · SRAM · bus
Clock-domain bridges
114 MHz compute domain
INT8 attention engine
K/V buffers on SRAM
Memory via bridges
Same QFN-64 pinout: the engine adds no pads
Status: design complete, in physical trials. DG32-2DOM has its own architecture deck and film.
Bit-exact
Each kick computes QKᵀ, softmax, the weighted sum and requantisation for a band of query rows, matching the software model exactly.
Up to 400 keys per head
One reciprocal per row keeps the INT8 datapath narrow enough to share one multiply array.
Never stalls control
Timing closed with positive slack at both 50 MHz and 114 MHz.
Sources: DG32-2DOM block architecture §1, §4.18–4.19; DG32-2DOM preliminary datasheet. Pre-silicon design values.
Notes: DG32-2DOM keeps everything in DG32-LITE and adds an INT8 attention engine on its own one hundred fourteen megahertz clock. It reaches memory through clock-domain-crossing bridges, so it never stalls the fifty megahertz control core. Its output is bit-exact to the software model, and timing closes at both clocks. It is designed for bearing-fault and anomaly detection inside the drive.

## Slide 14
14 · POSITIONING
DG32 leads on safety and trails on analog
DG32-LITE against the STM32G0 series, the incumbent entry-level motor-control MCU
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
14
DIMENSION
DG32-LITE
STM32G0 SERIES
WHAT IT MEANS
CPU
2 × RV32IM, hardware lockstep, 50 MHz
1 × Cortex-M0+, up to 64 MHz
Same class; DG32 spends core two on checking
Safety hardware
Lockstep comparator, fault latch, FAULT pin
Watchdogs, brown-out, software self-test
Lockstep otherwise means automotive MCUs
Motor PWM
3-phase + brake; 4 × DShot in hardware
Advanced timer; DShot in software
Equivalent PWM; DShot native on DG32
Math
Hardware CORDIC
None (appears on STM32G4)
FOC transforms run in hardware
On-chip AI
DG32-2DOM INT8 attention engine
None; AI runs in software
Condition monitoring inside the drive
Analog
8-bit SAR, ~200 kSa/s, 2 pins
12-bit, 2.5 MSa/s, up to 16 channels
G0 leads clearly; first roadmap item
Program memory
64 KB ROM + external QSPI flash
16–512 KB embedded flash
G0 leads; embedded flash on roadmap
Communications
2 × UART, SPI, I²C, QSPI
Up to 6 USART, USB FS, 2 × FDCAN
G0 leads; CAN-FD on roadmap
Source: DG32-LITE investor block diagram p2. STM32G0 column: public datasheet values (G0x1 / G0B1). DG32-LITE: design values, not measured.
Notes: Against the STM32G0, the entry-level incumbent, the comparison is honest. DG32 leads on hardware lockstep, native DShot, hardware CORDIC and the on-chip AI variant, with an open RISC-V core. The G0 leads clearly on its twelve-bit multi-channel ADC, embedded flash, USB and CAN-FD, and on production maturity.

## Slide 15
15 · ROADMAP
The next spin closes the two largest gaps
Where the incumbent leads most clearly is where the second spin starts
DEEPGRID SEMI · DG32-LITE ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
15
NOW
First silicon
September 2026 shuttle measures what simulation predicted
NEXT
Second spin
12-bit multi-channel ADC and embedded flash
THEN
Connectivity and debug
CAN-FD and interactive CPU debug
PARALLEL
DG32-2DOM
INT8 attention variant: design complete, physical trials
Gaps closed first
The analog front end and program memory are where the STM32G0 leads most clearly, so the second spin targets both before adding connectivity.
What this deck does not claim
No measured silicon results and no functional-safety certification. Every figure is a design value until first-silicon bring-up.
Source: DG32-LITE investor block diagram p2, roadmap to close the gap.
Notes: The roadmap works through those weaknesses, largest first. First silicon, on the September twenty twenty-six shuttle, tests the simulations against real parts. The following spin tackles the two largest gaps: an analog converter with twelve bits and several channels, and flash on the die. Only after that come CAN-FD and interactive debugging. DG32-2DOM advances meanwhile, its design finished and now in physical trials.

## Slide 16
16 · CLOSE
Safety in the core. Control in silicon.
Next milestone: first-silicon bring-up on the September 2026 shuttle turns these design values into measurements.
THREE THINGS TO REMEMBER
1 · Safety is in the core
Two RISC-V cores must agree on every committed store. A disagreement latches and drives FAULT_N within 39 simulated cycles.
2 · Control is in silicon
Sampling, transforms and PWM run in dedicated blocks, so one loop costs about 300 hardware cycles at any rate.
3 · The gaps are on the roadmap
A 12-bit ADC and embedded flash come first, then CAN-FD and debug. DG32-2DOM adds on-chip AI in the same footprint.
DEEPGRID SEMI · DG32-LITE ARCHITECTURE
16
Notes: Three ideas to hold on to. The protection is built into the processor itself, not bolted on in software. The costly parts of motor control are dedicated hardware, so the price of one loop is fixed and known in advance. And the weaknesses are named, with fixes scheduled. None of this has yet been measured on silicon, and no functional-safety certification is claimed; bring-up is where the numbers become real.