## Slide 1
DEEPGRID SEMI · SKU-1 · BLDC MOTOR CONTROLLER
One die runs the motor and drives its power stage.
A 130 nm BCD controller that runs field-oriented control in hardware and drives the high-voltage stage from the same die.
5 to 120 V
PRE-DRIVER RAIL
< 1 µs
HARDWARE PID
200 MHz
DGRIDRISCV HOST
PRE-SILICON ARCHITECTURE
Every figure in this deck is a design target. The motor control datapath is FPGA-validated; first multi-project wafer run, cycle 1.
DEEPGRID SEMI · SKU-1 ARCHITECTURE · OCTOBER 2026
Notes: SKU-1 is the BLDC motor controller in the DeepGrid portfolio. Headline and lede: SKU-1 product page. Figures: product page specs (5 V to 120 V pre-driver rail, hardware PID under 1 µs, DGridRiscV RV32IM at 200 MHz). Status: the portfolio status record for SKU-1 says the motor control datapath runs as circuit code on an FPGA and the part is in the first multi-project wafer run, cycle 1. Status: pre-silicon. Every figure is an architecture target from the SKU-1 product page, not a measurement.

## Slide 2
01 · WHAT IT IS
SKU-1 replaces a two-chip motor drive with one die
The microcontroller and gate pre-driver merge, and the control loop moves from firmware into hardware.
DEEPGRID SEMI · SKU-1 BLDC MOTOR CONTROLLER · PRE-SILICON ARCHITECTURE · OCTOBER 2026
02
The usual drive: two chips
A microcontroller runs the control loop in firmware.
A separate gate pre-driver drives the high-voltage stage.
SKU-1: one 130 nm BCD die
A hardware datapath closes the loop; the processor configures and supervises.
The same die drives the 5 V to 120 V stage.
Senses the rotor
Hall, quadrature or encoder input gives angle and speed. Three current-sense amplifiers and a 16-bit synchronised ADC digitise phase, bus and temperature.
Controls in hardware
PID, CORDIC and inverse Clarke and Park run as a datapath, so the loop closes in under 1 µs without waiting on firmware.
Drives up to 120 V
A buck-boost pre-driver rail spans 5 V to 120 V. Seven PWM channels feed three half-bridge pre-drivers, star or delta at runtime.
Notes: Source: SKU-1 product page, lede and block note; SKU-1 Architecture Guide, "What is SKU-1?". The product page states SKU-1 collapses the usual two-chip motor drive, a microcontroller plus a separate gate pre-driver, into one 130 nm BCD die, and that the processor configures and supervises but does not sit in the loop. Card figures come from the product page blocks and specs. Status: pre-silicon. Every figure is an architecture target from the SKU-1 product page, not a measurement.

## Slide 3
02 · WHY IT NEEDS ITS OWN SILICON
Three physical limits force a 130 nm BCD die
Each requirement of the motor drive has a direct consequence for how the die is built.
DEEPGRID SEMI · SKU-1 BLDC MOTOR CONTROLLER · PRE-SILICON ARCHITECTURE · OCTOBER 2026
03
REQUIREMENT
CONSEQUENCE FOR THE DIE
120 V
The pre-driver rail spans 5 V to 120 V.
That needs BCD power devices on the same die as the logic; thin-oxide advanced nodes cannot hold the voltage.
16-bit
A 16-bit ADC shares the die with a switching half-bridge.
Fast switching edges couple into the substrate, so the analog section needs guard rings and separate grounds.
< 1 µs
The control loop must close in under a microsecond.
PID, CORDIC and the Clarke and Park transforms run as a hardware datapath, not as firmware.
Together these set the part: 130 nm BCD / high-voltage CMOS, with the control loop built as hardware.
Notes: Source: SKU-1 product page, physics (requirement and consequence, three pairs), quoted. Process: product page specs, "130 nm BCD / high-voltage CMOS". Where the Technical Annex v3 sheet 2 labels the node "130 nm CMOS", the product page wins. Status: pre-silicon. Every figure is an architecture target from the SKU-1 product page, not a measurement.

## Slide 4
03 · SYSTEM ARCHITECTURE
Five zones, one bus, and no CPU in the loop
Redrawn from Technical Annex v3, sheet 2. Follow markers 1 to 4; F is the latched fault trip.
DEEPGRID SEMI · SKU-1 BLDC MOTOR CONTROLLER · PRE-SILICON ARCHITECTURE · OCTOBER 2026
04
Host commands: speed, torque, halt, brake, ramp
5 V to 120 V rail
HOST · CONTROL PLANE
DGridRiscV
RV32IM · 200 MHz
Timers · WDT · CCU
SRAM
32 KB, to 256 KB
ReRAM
256 KB, to 1 MB
Host interfaces
I²C · UART ×4 · SPI · CAN-FD ×2 · JTAG
MIXED SIGNAL
16-bit ADC
phase, bus, temp
DAC ×4
reference out
Temp sense
−40 to +125 °C
CSA ×3
current sense
POWER PATH
B-B converter
5 to 120 V rail
PWM ×7
to 200 kHz · 6 + 1 aux
Pre-drivers
R / Y / B half-bridges
Star / delta
runtime selectable
Protection
thermal · overcurrent · overvoltage → gate shutdown, latched
AXI bus · memory-mapped register file · 200 MHz
FIELD-ORIENTED CONTROL DATAPATH
PID tuner
hardware · < 1 µs
Rect → polar
CORDIC · magnitude + angle
d,q → 3-phase
inverse Park + Clarke
Sine / trapezoid
lookup · sine or 6-step
SENSOR + FEEDBACK
Hall / quad / enc
sensored or sensorless
Angle (ω)
rotor position + speed
iR iY iB rebuild
transfer function
Instant current
amplify + digitise
Commands reach the host: speed, torque, halt, brake.
Datapath: PID, CORDIC, inverse Park and Clarke, lookup.
PWM drives the three half-bridge pre-drivers.
Current and angle feedback closes the PID loop.
A thermal, overcurrent or overvoltage fault latches the gates off.
1
2
3
F
4
1
2
3
4
F
Notes: Source: SKU-1 diagram specification and SKU-1 Architecture Guide, "Architecture Overview" and the five component sections; figure redrawn from Technical Annex v3, sheet 2, as native editable shapes. Host control plane, mixed signal and power path sit on one AXI bus with a memory-mapped register file at 200 MHz; the field-oriented control datapath and the sensor feedback sit below it. Markers follow the guide's Key Data Flows: 1 commands reach the host; 2 the datapath turns the torque command into phase drive; 3 PWM drives the three half-bridge pre-drivers; 4 current and angle feedback closes the PID loop; F a thermal, overcurrent or overvoltage fault shuts the gates and latches. The processor configures and supervises; it does not sit in the loop. Status: pre-silicon. Every figure is an architecture target from the SKU-1 product page, not a measurement.

## Slide 5
04 · COMPONENTS
Four blocks carry the loop from sensor to gate
Signal flows from the sensors through the hardware datapath to the gate drive; the host configures it.
DEEPGRID SEMI · SKU-1 BLDC MOTOR CONTROLLER · PRE-SILICON ARCHITECTURE · OCTOBER 2026
05
Sensor + feedback
Hall, quadrature or encoder input, sensored or sensorless. An angle engine gives rotor position and speed; the three phase currents are rebuilt, amplified and digitised.
Mixed signal
A 16-bit synchronised ADC for phase, bus and temperature, four reference DACs, on-die temperature sense from −40 to +125 °C and three current-sense amplifiers.
Control datapath
Hardware PID with under 1 µs tuning latency, CORDIC rectangular to polar, inverse Park and Clarke, and sine or trapezoid lookup for sinusoidal or six-step drive.
Power path
Buck-boost pre-driver rail from 5 to 120 V. Seven PWM channels to 200 kHz, six bridge plus one auxiliary, three half-bridge pre-drivers, latched protection.
Host: DGridRiscV RV32IM at 200 MHz with timers and watchdog, 32 KB SRAM (to 256 KB), 256 KB ReRAM (to 1 MB), and I²C, UART ×4, SPI, CAN-FD ×2 and JTAG. It sets the loop up and supervises it.
Notes: Source: SKU-1 Architecture Guide, component sections (Sensor + feedback, Mixed signal, Field-oriented control datapath, Power path, Host control plane); SKU-1 product page blocks. Values: on-die temperature sense −40 to +125 °C; hardware PID under 1 µs tuning latency; PWM ×7 up to 200 kHz, six bridge plus one auxiliary; pre-drivers R, Y, B with per-phase clock gating; protection is thermal, overcurrent and overvoltage to a latched gate shutdown. Status: pre-silicon. Every figure is an architecture target from the SKU-1 product page, not a measurement.

## Slide 6
05 · DESIGN DECISIONS
Five design choices, each with a cost to test
What each architectural choice buys, and the engineering condition it creates for evaluation.
DEEPGRID SEMI · SKU-1 BLDC MOTOR CONTROLLER · PRE-SILICON ARCHITECTURE · OCTOBER 2026
06
DECISION
WHAT IT BUYS
WHAT IT ASKS OF THE DESIGN
Loop in a hardware datapath, processor outside it
Fixed loop latency, under 1 µs
The 1 µs deadline must hold while the processor runs CAN-FD traffic on the same bus
130 nm BCD, not an advanced node
Logic and 5 V to 120 V power devices on one die
Guard rings and separate grounds keep switching edges out of the 16-bit ADC
ReRAM for stored parameters
256 KB on die, expandable to 1 MB
ECC and scrubbing, because retention falls quickly above 125 °C junction
Three half-bridge pre-drivers on die
No second gate-driver chip
Dead-time insertion fine enough to hold as gate thresholds drift with temperature
Sine or trapezoid lookup; star or delta at runtime
Sinusoidal or six-step drive, either winding, one part
Mode and winding are set by the host at configuration, not inside the loop
Rows 1 to 4 are the four questions on slide 9. None is answered yet; each needs simulation, layout or silicon data.
Notes: Source: SKU-1 product page physics, blocks, specs and questions; SKU-1 Architecture Guide, "Why it exists" lines for the host, power path and datapath. The "what it asks of the design" column restates the four engineering questions on the product page (substrate isolation, loop deadline under bus load, ReRAM at temperature, shoot-through); the fifth row restates the guide: star or delta winding selection is runtime selectable and the waveform lookup offers sinusoidal or six-step drive. Status: pre-silicon. Every figure is an architecture target from the SKU-1 product page, not a measurement.

## Slide 7
06 · KEY DATA FLOW
Torque command reaches the gates in four steps
Steps 2 to 4 are hardware; the hardware PID tuning latency target is under 1 µs.
DEEPGRID SEMI · SKU-1 BLDC MOTOR CONTROLLER · PRE-SILICON ARCHITECTURE · OCTOBER 2026
07
Command
Speed, torque, halt and brake commands reach the host over its interfaces.
Compute
The datapath turns the torque command into phase drive: PID, CORDIC, inverse Park and Clarke, waveform lookup.
Drive
PWM, seven channels to 200 kHz, drives the three half-bridge pre-drivers.
Feedback
Phase current and rotor angle feed back and close the PID loop.
1
2
3
4
F · Fault path
A thermal, overcurrent or overvoltage fault shuts the gates and latches. The trip sits in the power path, beside the pre-drivers.
Where the processor sits
The DGridRiscV core configures the loop and supervises it. Steps 2 to 4 run without it, so the loop latency is fixed.
Notes: Source: SKU-1 Architecture Guide, "Key Data Flows" (markers 1 to 4 and F), and the Field-oriented control datapath section: "The loop runs in hardware, so its latency is fixed and stays under 1 µs." Product page block note: the processor configures and supervises; it does not sit in the loop. Status: pre-silicon. Every figure is an architecture target from the SKU-1 product page, not a measurement.

## Slide 8
07 · ARCHITECTURE TARGETS
Every figure is a target; none is measured yet
Architecture targets from the SKU-1 product page. No figure below comes from measured silicon.
DEEPGRID SEMI · SKU-1 BLDC MOTOR CONTROLLER · PRE-SILICON ARCHITECTURE · OCTOBER 2026
08
PARAMETER
ARCHITECTURE TARGET
STATUS
Process
130 nm BCD / high-voltage CMOS
Target
High-voltage rail
5 V to 120 V, buck-boost pre-driver
Target
Processor
DGridRiscV (RV32IM) at 200 MHz
Target
Memory
32 KB SRAM (to 256 KB), 256 KB ReRAM (to 1 MB)
Target
Conversion
16-bit synchronised ADC, three current-sense amplifiers
Target
Control engine
Hardware PID under 1 µs, CORDIC, inverse Clarke and Park
Target
PWM
Seven channels to 200 kHz (six-switch bridge plus one auxiliary)
Target
DESIGNED TOWARD
Not held. No certificate exists for any DeepGrid part.
AEC-Q100 Grade 0
ISO 26262 ASIL-B/C
UL94
Standards the design is developed toward. Meeting them needs silicon, test and qualification.
Notes: Source: SKU-1 product page specs (seven rows, quoted) and designedToward list. SKU-1 Architecture Guide header: "Every value is a design target, not a measurement. Standards appear only as targets the design is developed toward; no certificate exists for any DeepGrid part." Status: pre-silicon. Every figure is an architecture target from the SKU-1 product page, not a measurement.

## Slide 9
08 · EVALUATION
Four questions decide if SKU-1 fits your drive
The engineering questions the SKU-1 architecture sheet asks of itself, for your evaluation.
DEEPGRID SEMI · SKU-1 BLDC MOTOR CONTROLLER · PRE-SILICON ARCHITECTURE · OCTOBER 2026
09
1 · Substrate isolation
Which guard-ring and deep-trench structures keep 10 V/ns switching edges on the 120 V half-bridge out of the 16-bit ADC?
2 · Loop deadline under bus load
Does the CORDIC datapath still meet its 1 µs deadline while the processor runs CAN-FD traffic over the same bus?
3 · ReRAM at temperature
Retention falls quickly above 125 °C junction. What ECC and scrubbing keep stored parameters intact in continuous operation?
4 · Shoot-through
How fine is dead-time insertion, and does it hold as gate thresholds drift with temperature?
Each question maps to one design decision on slide 6. Ask for the answer as simulation, layout or test data, and note which kind it is.
Notes: Source: SKU-1 product page, questions (four, quoted verbatim): substrate isolation, loop deadline under bus load, ReRAM at temperature, shoot-through. The figures in them (10 V/ns edges, 120 V half-bridge, 16-bit ADC, 1 µs deadline, 125 °C junction) are from the same record. Status: pre-silicon. Every figure is an architecture target from the SKU-1 product page, not a measurement.

## Slide 10
09 · NEXT STEP
Evaluate the loop and the isolation first
One die, a hardware loop and a 120 V stage: worth testing on the four questions before design-in.
DEEPGRID SEMI · SKU-1 BLDC MOTOR CONTROLLER · PRE-SILICON ARCHITECTURE · OCTOBER 2026
10
NEXT STEP
Scope an evaluation against the four questions.
Request the SKU-1 architecture guide and Technical Annex v3, sheet 2. Bring your rail voltage, winding and loop-rate needs.
CONTACT
group@deepgrid.in
One die, two jobs
Field-oriented control and the 5 V to 120 V gate drive share one 130 nm BCD die.
The loop is hardware
PID, CORDIC and inverse Clarke and Park close the loop in under 1 µs; the processor stays outside it.
Pre-silicon, stated plainly
Every figure is a design target and standards are designed toward, not held. The motor control datapath is FPGA-validated.
Notes: Summary of slides 1 to 9. Sources: SKU-1 product page (headline, lede, specs, designedToward, questions); SKU-1 Architecture Guide; portfolio status record for SKU-1 (motor control datapath FPGA-validated; first multi-project wafer run, cycle 1). Contact address from the DeepGrid site contact page. Status: pre-silicon. Every figure is an architecture target from the SKU-1 product page, not a measurement.