## Slide 1
DEEPGRID SEMI · SKU-2 SMART-METER SOC · SYSTEM ARCHITECTURE
One die that measures, signs
and keeps time
A meter that keeps measuring, and keeps its record, when the mains is gone.
6 × 24-bit
SIGMA-DELTA CHANNELS
Class 0.5S target, sinc³ at OSR 256
200 MHz
DGRIDRISCV CORE
AES-256 and SHA, secure boot
< 2 µW
ALWAYS-ON DOMAIN
Clock and tamper log on a backup cell
STATUS
Pre-silicon. Every figure in this deck is an architecture target, not a measurement. The meter measurement chain is FPGA-validated; the 130 nm die is planned for the Cycle-1 wafer run alongside SKU-1.
DEEPGRID SEMI · SKU-2 SMART-METER SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
01
Notes: SKU-2 is a smart-meter system-on-chip: metrology, compute and security, and an always-on clock domain on one 130 nm CMOS die.
Headline: product page SKU-2, headline and lede. Figures: product page specs (front end, processor, always-on domain).
Status: the site's applications record for SKU-2 (status "Cycle-1 wafer run, alongside SKU-1"; evidence "FPGA-validated: the meter measurement chain runs as circuit code on the same Artix-7").
Say plainly: pre-silicon. Every value is a design target (architecture guide, scope note).

## Slide 2
One chip replaces a front end and a meter MCU
Measurement, security and the meter's own time base on one 130 nm CMOS die.
DEEPGRID SEMI · SKU-2 SMART-METER SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
02
01 · WHAT IT IS
Measure
Six 24-bit sigma-delta channels and sinc³ decimation at OSR 256 feed a metrology engine for active, reactive and apparent power, and harmonics to the 15th.
DG-AFE6 · DECIM · METRO
Secure
A DGridRiscV core at 200 MHz with a four-channel DMA and an AES-256 and SHA engine stores and signs every reading, with secure boot and tamper key erase.
DGridRiscV · DMA · DG-SE
Keep time
An isolated always-on domain under 2 µW runs the clock on a 32.768 kHz crystal and senses tamper from a 2.2 to 3.6 V backup cell.
PMU + RTC · tamper sense
WHAT A METER USES TODAY
A metrology front end plus a separate meter microcontroller: two parts to power, secure and keep in time.
WITH SKU-2
One die for measurement, security and its own time base, on a 32-bit AHB-Lite multilayer bus.
Evidence today: pre-silicon. The meter measurement chain is FPGA-validated; no figure in this deck is a silicon measurement.
Notes: One chip where a meter uses two today.
Cards: product page SKU-2, blocks (Metrology; Compute and security; Always-on domain) and blockNote ("stored and signed by the security engine").
"Replaces": the site's applications record for SKU-2 ("A metrology front end plus a separate meter microcontroller").
Bus: architecture guide, Key Data Flows step 4 (32-bit bus) and product page specs (AHB-Lite multilayer bus).
The two-chip consequence line is a fair reading of the replaces record, not a measured comparison: no BOM or power comparison is claimed.

## Slide 3
Three meter requirements dictate the silicon
Requirement on the left, the consequence in silicon on the right, and the block that carries it.
DEEPGRID SEMI · SKU-2 SMART-METER SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
03
02 · WHY ITS OWN SILICON
THE METER REQUIRES
SO THE SILICON NEEDS
WHERE IT LANDS
Class 0.5S accuracy across a 1000:1 current range.
A sigma-delta converter with low flicker noise and stable references, calibrated once for a long service life.
Metrology zone
DG-AFE6, six 24-bit channels
The clock and tamper log must survive outages on a backup cell.
An isolated always-on domain drawing under 2 µW, separate from the 200 MHz core.
Always-on zone
PMU + RTC on 32.768 kHz
Open 130 nm processes have no embedded flash.
Code lives in ROM, ECC SRAM and encrypted external QSPI, or in SCL non-volatile memory where available.
Memory plan
ROM · ECC SRAM · QSPI, or SCL NVM
Each block on the next slide answers one of these three requirements. None is there for its own sake.
Notes: The physics forces the architecture.
Requirement and consequence rows: product page SKU-2, physics (all three pairs, verbatim).
"Where it lands": product page blocks and specs; architecture guide, Architecture Overview items 1 to 3.
Class 0.5S is a target the design is developed toward, not a certificate (architecture guide, Designed toward).

## Slide 4
Measurement, security and time share one bus
Six-channel metrology, compute and security, and an always-on domain on a 32-bit AHB-Lite multilayer bus.
DEEPGRID SEMI · SKU-2 SMART-METER SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
04
03 · SYSTEM ARCHITECTURE
METROLOGY
DG-AFE6
6-ch 24-bit sigma-delta
DECIM
sinc³ · OSR 256
METRO
P Q S · THD to 15th
COMPUTE + SECURITY
DGridRiscV
RV32IM_Zicsr
DMA
4-channel
DG-SE
AES-256 · SHA-256
ALWAYS-ON
PMU + RTC
32.768 kHz XTAL · brownout 2.0 V · < 2 µW
AHB-Lite multilayer bus · 32-bit · 200 MHz
PERIPHERALS
RTC
tamper log
Timer
capture / compare
LCD
4 × 40 segment
UART
DLMS / COSEM
Tamper
case · magnet
GPIO
relay + LED
V / I sense · 6 channels
1
2
3
4
5
1
Six voltage and current channels enter the front end.
2
The 24-bit samples decimate through sinc³ at OSR 256.
3
The metrology engine computes P, Q, S and THD.
4
Results cross the 32-bit bus to the core and DMA.
5
Readings leave on the DLMS/COSEM UART.
Notes: Read it top-left to bottom: markers 1 to 5 trace one measurement from the sense inputs to the meter UART.
Structure: redrawn from the Technical Annex v3, sheet 3, through the site's diagram spec for SKU-2 (zones, blocks, edges and markers).
Values: product page SKU-2 and the SKU-2 architecture guide (Architecture Overview; Key Data Flows 1 to 5).
The bus label omits the annex's master and slave count, which is not on the product page or in the guide.
Zone colours: teal metrology, blue compute and security, amber always-on, grey peripherals; cyan is the measurement path. Every value is a design target.

## Slide 5
Four zones, each with one job it cannot share
What each zone does and why it is there, with the blocks that carry it.
DEEPGRID SEMI · SKU-2 SMART-METER SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
05
04 · INSIDE THE PART
ZONE 1
Metrology
A six-channel 24-bit sigma-delta front end, a sinc³ decimator at OSR 256, and a metrology engine for P, Q, S and THD to the 15th harmonic. Why: billing accuracy is set by the converter and the arithmetic, so both are dedicated hardware.
DG-AFE6 6-ch 24-bit · DECIM sinc³ OSR 256 · METRO P Q S, THD-15
ZONE 2
Compute + security
A DGridRiscV core at 200 MHz, a four-channel DMA and the DG-SE security engine. Readings are stored and signed by the security engine; secure boot and tamper key erase protect the keys.
DGridRiscV RV32IM_Zicsr · DMA 4-ch · DG-SE AES-256, SHA-256
ZONE 3
Always-on
A PMU and RTC on a 32.768 kHz crystal with brownout detection, drawing under 2 µW from a 2.2 to 3.6 V backup cell. Why: time and tamper state must survive when mains power is gone.
PMU + RTC · brownout 2.0 V · tamper sense
ZONE 4
Peripherals
A tamper-logging RTC, a capture and compare timer, a 4 × 40 segment LCD, the DLMS/COSEM UART, an optical port, case and magnet tamper inputs, and GPIO for relay and LED.
RTC · Timer · LCD · UART · Tamper · GPIO
Notes: Four zones, one job each.
Text: SKU-2 architecture guide, Component sections (Metrology; Compute + security; Always-on; Peripherals), "What it does" and "Why it exists".
Backup range, optical port and the stored-and-signed sentence: product page SKU-2, blocks and blockNote.
All values are architecture targets from the Technical Annex v3, sheet 3, as carried by the product page.

## Slide 6
Four decisions, and what each asks of the meter
Each choice, the alternative it rules out, the reason, and the check an evaluator should run.
DEEPGRID SEMI · SKU-2 SMART-METER SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
06
05 · DESIGN DECISIONS
DECISION
INSTEAD OF
WHY
WHAT TO VERIFY
Metrology in dedicated hardware
Energy arithmetic in firmware on the core
Billing accuracy is set by the converter and the arithmetic, so both are dedicated hardware.
Class 0.5S held across a 1000:1 current range over the service life.
An isolated always-on domain under 2 µW
One power domain for the whole die
The clock and tamper log must survive outages on a backup cell, apart from the 200 MHz core.
Leakage across the isolation cells during a thirty-day outage.
Code in ROM, ECC SRAM and encrypted QSPI, or SCL non-volatile memory
Embedded flash
Open 130 nm processes have no embedded flash.
Which code-storage option ships first.
Metrology, security and time base on one die
A front end plus a separate meter MCU
A meter needs one chip for measurement, security and its own time base.
How a magnet or injected DC is detected while measurement is preserved.
Each "What to verify" is one of the four evaluator questions on slide 9.
Notes: Four decisions, each with a check.
Row 1: architecture guide, Component: Metrology, "Why it exists"; product page physics 1 and question "Accuracy over a lifetime".
Row 2: product page physics 2; question "Blackout retention".
Row 3: product page physics 3; question "Non-volatile memory".
Row 4: product page lede; the site's applications record for SKU-2 (replaces); question "Magnetic and DC tamper".
The "Instead of" column names the alternative each decision rules out; it is a reading of the sources, not a measured comparison.

## Slide 7
One reading takes five steps from pin to UART
The measurement path, numbered as on the system diagram, and what stays alive in an outage.
DEEPGRID SEMI · SKU-2 SMART-METER SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
07
06 · KEY DATA FLOW
1
Sense
Six voltage and current channels enter DG-AFE6.
2
Decimate
24-bit samples pass sinc³ at OSR 256.
3
Compute
METRO forms P, Q, S and THD to the 15th.
4
Cross the bus
Results reach the core and DMA over 32-bit AHB-Lite.
5
Leave
Readings go out on the DLMS/COSEM UART.
On the core side
Results reach the DGridRiscV core and the four-channel DMA. The security engine stores and signs them with AES-256 and SHA-256 before they leave on the UART, and the same readings drive the 4 × 40 segment LCD.
Path markers 4 and 5
When the mains is gone
The always-on domain keeps time and tamper state when everything else is off: the RTC on a 32.768 kHz crystal, brownout detection at 2.0 V, and case and magnet tamper sense, under 2 µW from a 2.2 to 3.6 V backup cell.
Always-on zone
Notes: One reading, five steps; then what survives an outage.
Steps 1 to 5: SKU-2 architecture guide, Key Data Flows; the same markers as the system diagram (diagram spec for SKU-2, markers).
"On the core side": product page blockNote ("decimated and turned into energy figures, and are stored and signed by the security engine"); guide, Compute + security (AES-256, SHA-256); product page blocks (4 x 40 segment LCD). The LCD line describes where readings are displayed; display update timing is not specified in the sources.
"When the mains is gone": product page blockNote ("The always-on domain keeps time and tamper state when everything else is off") and blocks; guide, Component: Always-on (brownout 2.0 V).

## Slide 8
Every figure here is a target, not a measurement
Seven rows from the product page specification, each one labelled a target.
DEEPGRID SEMI · SKU-2 SMART-METER SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
08
07 · ARCHITECTURE TARGETS
PARAMETER
ARCHITECTURE TARGET
STATUS
Process
130 nm CMOS
Target
Front end
Six-channel 24-bit sigma-delta, sinc³ OSR 256
Target
Accuracy class
Class 0.5S target (P, Q, S, THD to 15th harmonic)
Target
Processor
DGridRiscV at 200 MHz, AHB-Lite multilayer bus
Target
Always-on domain
Under 2 µW, 32.768 kHz, 2.2 to 3.6 V backup
Target
Security
AES-256, SHA, secure boot, tamper key erase
Target
Interfaces
DLMS/COSEM UART, 4 × 40 segment LCD, optical port
Target
Designed toward
IEC metering accuracy Class 0.5S. A target the design is developed toward, not a certificate held; no certificate exists for any DeepGrid part.
Evidence today
Pre-silicon. The meter measurement chain is FPGA-validated. The 130 nm die is planned for the Cycle-1 wafer run alongside SKU-1.
Every row is an architecture target from the Technical Annex v3, sheet 3, as stated on the product page. None is a silicon measurement.
Notes: Targets, not measurements.
Table: product page SKU-2, specs (all seven rows, verbatim values).
Designed toward: product page designedToward; architecture guide, Designed toward and scope note ("no certificate exists for any DeepGrid part").
Evidence today: the site's applications record for SKU-2 (status and evidence fields).

## Slide 9
Four questions decide whether SKU-2 fits your meter
Put these to DeepGrid before committing bench time. Each tests one zone of the architecture.
DEEPGRID SEMI · SKU-2 SMART-METER SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
09
08 · EVALUATOR QUESTIONS
Accuracy over a lifetime
How does the front end hold Class 0.5S across a 1000:1 current range without drift over a fifteen-year service life?
Tests the Metrology zone
1
Magnetic and DC tamper
When a strong magnet or injected DC tries to defeat metrology, how is the imbalance detected and measurement preserved?
Tests Metrology and the tamper inputs
2
Blackout retention
What leakage crosses the isolation cells into the always-on domain during a thirty-day outage on the backup cell?
Tests the Always-on zone
3
Non-volatile memory
Which code-storage option ships first: ROM with encrypted QSPI, or SCL non-volatile memory?
Tests the memory plan
4
These are the questions the architecture sheet asks of itself. Each needs silicon or a dated plan to settle.
Notes: Four questions, verbatim from the product page SKU-2, questions (titles and wording unchanged).
The "Tests" line maps each question to the zone on slides 4 and 5 that must answer it.
"Each needs silicon or a dated plan to settle" follows from the pre-silicon status (architecture guide scope note).

## Slide 10
09 · NEXT STEP
Evaluate it against your meter's three hard limits
Bring three things to the first call: your accuracy class and current range, the tamper cases your tender names, and the outage your clock and tamper log must survive.
DISCUSS THIS PART
group@deepgrid.in
Subject: SKU-2 smart-meter SoC
WHAT TO TAKE AWAY
Measures
Six 24-bit sigma-delta channels and a metrology engine, designed toward Class 0.5S across 1000:1.
Secures
A 200 MHz DGridRiscV core with AES-256 and SHA, secure boot and tamper key erase.
Keeps time
An always-on domain under 2 µW keeps the clock and tamper log through an outage.
Status
Pre-silicon. Every figure is an architecture target; the measurement chain is FPGA-validated.
DEEPGRID SEMI · SKU-2 SMART-METER SOC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
10
Notes: One action: evaluate SKU-2 against the meter's accuracy, tamper and outage limits.
Contact: the site's contact page addresses group@deepgrid.in; the product page "Discuss this part" button carries the part name.
Summary lines: product page SKU-2 (lede, specs, designedToward); status: the site's applications record for SKU-2.
Do not imply a datasheet, a certificate or a delivery date; none exists.