## Slide 1
DEEPGRID SEMI · SKU-3 · HI-REL POWER-MANAGEMENT IC
One die turns a 28 V bus into four supervised rails
Architecture targets for avionics and vehicle electronics: input conditioning, a peak-current-mode pre-regulator, four monitored rails and an upset-hardened sequencer on 180 nm BCD.
PRE-SILICON · EVERY FIGURE IS A DESIGN TARGET, NOT A MEASUREMENT
28 V
NOMINAL BUS IN
4.5 to 40 V continuous; 80 V surge; 100 V spike
4 rails
SEQUENCED OUTPUTS
5 V 2 A · 3.3 V 3 A · 1.8 V 500 mA · 1.2/0.9 V 300 mA
12 ppm/°C
REFERENCE DRIFT
Curvature-corrected bandgap, −55 to +125 °C
4-step
HARDENED SEQUENCER
Triple-redundant state machine on DICE latches
DEEPGRID SEMI · SKU-3 HI-REL PMIC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
01
Notes: SKU-3 is DeepGrid's high-reliability power management IC for avionics and vehicle electronics. One 180 nm BCD die takes the 28 V equipment bus and produces four sequenced, supervised rails.
Say plainly: this is pre-silicon. The development status is a prototype on 130 nm 20 V devices, then production at SCL 180 nm. No measured silicon result exists; every number in this deck is an architecture target.
Sources: product page record (sku3) headline, lede and specs; SKU-3 Architecture Guide, "What is SKU-3?"; Technical Annex v3, sheet 4.

## Slide 2
01 · WHAT IT IS
One die conditions, converts and supervises
SKU-3 is a high-reliability power management IC for avionics and vehicle electronics.
DEEPGRID SEMI · SKU-3 HI-REL PMIC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
02
Condition the bus
An EMI filter and TVS clamp, an ideal-diode reverse-polarity stage, soft-start inrush control, and under- and over-voltage lockout at 18 V and 34 V.
Convert to four rails
A peak-current-mode synchronous buck pre-regulates at 500 kHz to 2 MHz. Two bucks and two LDOs then produce the board supplies.
Supervise every rail
Each rail has a window monitor, a current limit and power-good. A triple-redundant four-step sequencer decides when each rail may start.
THE FOUR RAILS · ARCHITECTURE TARGETS
5.0 V
BUCK · 2 A
3.3 V
BUCK · 3 A
1.8 V
LDO · 500 MA
1.2/0.9 V
LDO · 300 MA
Source: product specification (SKU-3) and SKU-3 Architecture Guide. Pre-silicon design targets.
Notes: Three jobs sit on one die. First it conditions the bus: EMI and TVS clamp, ideal diode for reverse polarity, inrush limiting, and hysteretic UVLO and OVLO at 18 V and 34 V. Second it converts: a synchronous buck pre-regulator, then two bucks at 5 V and 3.3 V and two LDOs at 1.8 V and 1.2 or 0.9 V. Third it supervises: window monitors, current limits, power-good, and a four-step triple-redundant sequencer.
Rail currents are targets: 5 V at 2 A, 3.3 V at 3 A, 1.8 V at 500 mA, 1.2 or 0.9 V at 300 mA.
Sources: product page record (sku3) lede and blocks; SKU-3 Architecture Guide, "What is SKU-3?" and "Architecture Overview" items 1 to 5.

## Slide 3
02 · WHY IT NEEDS ITS OWN SILICON
Bus physics picks the process, not the logic
Three requirements from the bus and the environment each force one silicon choice.
DEEPGRID SEMI · SKU-3 HI-REL PMIC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
03
REQUIREMENT
SILICON CONSEQUENCE
INPUT STRESS
The input sees 4.5 to 40 V continuous, 80 V surges and 100 V spikes.
A 180 nm BCD process with 30 V power devices and an input stage that clamps without thermal runaway.
REFERENCE STABILITY
A 12 ppm/°C reference from −55 to +125 °C.
A curvature-corrected bandgap with large matched resistors, a mature-node strength.
UPSET IMMUNITY
A single particle strike must not corrupt the power sequence.
Dual interlocked latches and triple-modular redundancy on the sequencer state machine.
Source: product specification (SKU-3), physical requirements. Pre-silicon design targets.
Notes: This is why SKU-3 is its own die rather than a generic regulator plus logic. Each requirement forces one choice.
Input stress: 4.5 to 40 V continuous with 80 V surges and 100 V spikes needs 30 V power devices on 180 nm BCD and an input stage that clamps without thermal runaway.
Reference stability: 12 ppm/°C from −55 to +125 °C needs a curvature-corrected bandgap with large matched resistors, which a mature node does well.
Upset immunity: one particle strike must not corrupt the power sequence, so the sequencer uses DICE latches and triple-modular redundancy. The annex states there is no radiation-hardness claim beyond that hardening by design.
Sources: product page record (sku3) physics; Technical Annex v3, sheet 4 (status and node path).

## Slide 4
03 · SYSTEM ARCHITECTURE
Power flows down; status flows back up
Five zones on one die: the bus enters at 1; every rail reports power-good to the sequencer at 4.
DEEPGRID SEMI · SKU-3 HI-REL PMIC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
04
INPUT CONDITIONING
EMI + TVS
clamp 36 V
Ideal diode
reverse polarity
Inrush
soft-start, dI/dt limit
UVLO + OVLO
18 V / 34 V
PRE-REGULATOR · SYNCHRONOUS BUCK
Error amp
type-III · 60 dB DC
PWM comp
+ slope comp
Gate driver
20 ns non-overlap
Current sense
cycle-by-cycle limit
Power stage
LDMOS half-bridge · 500 kHz to 2 MHz
REFERENCE + BIAS
Bandgap
1.20 V · 12 ppm/°C
Trim
OTP 6-bit
Bias
PTAT + CTAT
Osc
RC 8 MHz · ±2%
RAIL GENERATION
Buck · 5 V
2 A · soft-start
Window monitor
OV / UV · ±3%
OC limit
foldback → PG
Buck · 3.3 V
3 A · soft-start
Window monitor
OV / UV · ±3%
OC limit
foldback → PG
LDO · 1.8 V
500 mA · soft-start
Window monitor
OV / UV · ±3%
OC limit
foldback → PG
LDO · 1.2 / 0.9 V
300 mA · soft-start
Window monitor
OV / UV · ±3%
OC limit
foldback → PG
SUPERVISION · SEQUENCING · TELEMETRY
Sequencer
4-step order · TMR
Telemetry
10-bit SAR · 500 kSPS · SPI
Watchdog
windowed · 1 / 10 ms
SEU harden
DICE latches · TMR on FSM
28 V aircraft bus
READING PATH
The 28 V bus enters input conditioning.
The conditioned bus feeds the pre-regulator.
The pre-regulator output feeds the four rail regulators.
Each rail reports power-good to the sequencer through its window monitor and current limit.
Current sense closes the peak-current-mode inner loop.
The sequencer decides when each rail may start.
1
2
3
5
4
1
2
3
4
5
Redrawn from Technical Annex v3, sheet 4. Rail, telemetry and sequencer values follow the product specification. All values are design targets.
Notes: Read it by the numbers. 1: the 28 V bus enters input conditioning. 2: the conditioned bus feeds the pre-regulator. 3: the pre-regulator output feeds the four rail regulators. 4: each rail reports power-good to the sequencer through its window monitor and current limit. 5: current sense closes the peak-current-mode inner loop.
Power flows down from the bus through conditioning and the pre-regulator into four rails; status flows back up, and the hardened sequencer decides when each rail may start.
Where this differs from the annex sheet: structure follows sheet 4, but some values on that sheet differ and this deck follows the product specification. The sheet draws 3V3 and 1V8 LDOs at 2 A and 3 A and 1V2 and 0V9 bucks at 5 A and 6 A; the product specification states 5 V and 3.3 V bucks at 2 A and 3 A and 1.8 V and 1.2 or 0.9 V LDOs at 500 mA and 300 mA. The sheet shows a 12-bit telemetry ADC (10-bit at 500 kSPS here) and 8 sequencer slots (4 steps here).
Sources: SKU-3 Architecture Guide, "Architecture Overview" and "Key Data Flows"; diagram spec scripts/sku-diagrams/specs.py (sku3); Technical Annex v3, sheet 4.

## Slide 5
04 · COMPONENTS
Each block stops one fault reaching the board
Four blocks, colour-keyed to the architecture diagram; each one exists to contain a specific failure.
DEEPGRID SEMI · SKU-3 HI-REL PMIC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
05
Input conditioning
Stops bus surges and spikes reaching the rails.
EMI filter and TVS clamp at 36 V; back-to-back LDMOS ideal diode for reverse polarity; dI/dt-limited soft-start; UVLO and OVLO at 18 V / 34 V, hysteretic.
Pre-regulator
Limits current cycle by cycle, so a downstream fault cannot run away.
Type-III error amp, 60 dB DC; PWM comparator with slope compensation, 500 kHz to 2 MHz; adaptive dead-time driver, 20 ns non-overlap; LDMOS half-bridge; sense-FET current sense.
Rail generation
Catches a rail that drifts or overloads before the board depends on it.
Bucks at 5 V 2 A and 3.3 V 3 A; LDOs at 1.8 V 500 mA and 1.2 or 0.9 V 300 mA. Each: soft-start, ±3% OV/UV window monitor, foldback current limit to power-good.
Reference, telemetry, supervision
Keeps a single-event upset from reordering or dropping a rail.
Brokaw bandgap 1.20 V, 12 ppm/°C, OTP 6-bit trim; 8 MHz RC oscillator ±2%; 10-bit 500 kSPS ADC on V, I and die temperature over SPI; windowed watchdog; DICE latches, TMR sequencer.
Source: SKU-3 Architecture Guide, component sections; product specification (SKU-3). Pre-silicon design targets.
Notes: Each block has a fault it is there to contain.
Input conditioning: an aircraft bus carries surges and spikes the downstream rails must never see. EMI and TVS clamp at 36 V, ideal diode, inrush limiting, UVLO and OVLO at 18 V and 34 V.
Pre-regulator: peak-current-mode control limits current cycle by cycle, so a fault downstream cannot run away. Type-III error amp at 60 dB DC, slope-compensated PWM comparator at 500 kHz to 2 MHz, 20 ns non-overlap gate drive, LDMOS half-bridge, sense-FET current sense.
Rail generation: each of the four rails has a soft-start ramp, a plus or minus 3% over- and under-voltage window monitor and a foldback current limit that reports power-good. The phrase "before the board depends on it" is our synthesis of that monitoring role.
Supervision: a single-event upset must not reorder or drop a rail, so the sequencer state is hardened by design with DICE latches and TMR. Watchdog window is 1 ms / 10 ms. Reference: Brokaw bandgap at 1.20 V, 12 ppm/°C, one-time 6-bit OTP trim after packaging; 8 MHz RC oscillator trimmed to plus or minus 2%.
Sources: SKU-3 Architecture Guide, "Component" sections; product page record (sku3) blocks.

## Slide 6
05 · DESIGN DECISIONS
Each design choice buys robustness at a cost
Four architecture choices, what each protects against, and what it asks of the design.
DEEPGRID SEMI · SKU-3 HI-REL PMIC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
06
DECISION
WHAT IT BUYS
WHAT IT COSTS
180 nm BCD, 30 V power devices
Survives 4.5 to 40 V continuous with 80 V surges; production planned at SCL Mohali.
Prototyping runs first on 130 nm 20 V devices; the input stage must clamp without thermal runaway.
Peak-current-mode pre-regulator
A cycle-by-cycle current limit: a fault downstream cannot run away.
Needs slope compensation and a type-III loop; margin must hold across capacitor types and temperature.
Curvature-corrected Brokaw bandgap
12 ppm/°C from −55 to +125 °C, the reference every rail is regulated against.
Large matched resistors spend die area; the 6-bit OTP trim is one-time, after packaging.
DICE latches and TMR sequencer
One particle strike cannot reorder or drop a rail.
Three copies of the sequencer state plus voting; layout spacing must keep one strike off two voting bits.
Source: product specification (SKU-3), physics and specs; SKU-3 Architecture Guide, component sections. Costs follow from the named mechanism.
Notes: Every choice here buys robustness and asks something of the design; the costs are what to probe in evaluation.
Process: 180 nm BCD with 30 V power devices survives the 4.5 to 40 V input with 80 V surges; production is planned at SCL Mohali and prototyping uses 130 nm 20 V devices first. The input stage must clamp the 100 V spike without thermal runaway.
Control: peak-current-mode gives a cycle-by-cycle limit, but needs slope compensation and type-III compensation; the open question is phase and gain margin across capacitor types and temperature.
Reference: the curvature-corrected bandgap reaches 12 ppm/°C using large matched resistors; trim is 6-bit OTP, one-time, post-package.
Upset hardening: DICE latches and TMR triple the sequencer state and vote on it; layout spacing has to stop one heavy-ion strike flipping two of three voting bits.
The "what it costs" column is a fair reading of each named mechanism, not a measured penalty.
Sources: product page record (sku3) physics, specs and questions; SKU-3 Architecture Guide, component sections.

## Slide 7
06 · KEY DATA FLOW
Five steps take power from the bus to a good rail
Steps 1 to 4 carry power and status; step 5 is the inner current loop inside the pre-regulator.
DEEPGRID SEMI · SKU-3 HI-REL PMIC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
07
1
Bus in
The 28 V bus enters input conditioning.
2
Conditioned
The conditioned bus feeds the pre-regulator.
3
Pre-regulated
The pre-regulator output feeds the four rail regulators.
4
Power-good
Each rail reports power-good to the sequencer through its window monitor and current limit.
5
Inner loop
Current sense closes the peak-current-mode inner loop.
What the board sees
The hardened sequencer decides when each rail may start, and every rail reports back through its window monitor.
What stays inside the die
Current sense feeds the error amplifier every switching cycle, so the pre-regulator limits current before a fault spreads.
Source: SKU-3 Architecture Guide, "Key Data Flows" markers 1 to 5; product specification block note.
Notes: Walk the five steps. 1: the 28 V bus enters input conditioning. 2: the conditioned bus feeds the pre-regulator. 3: the pre-regulator output feeds the four rail regulators. 4: each rail reports power-good to the sequencer through its window monitor and current limit. 5: current sense closes the peak-current-mode inner loop.
Steps 1 to 4 are the outer path; step 5 is the inner loop and runs every switching cycle (500 kHz to 2 MHz target).
The point for a board designer: power-good is reported, not assumed. The sequencer decides when each rail may start.
Sources: SKU-3 Architecture Guide, "Key Data Flows"; product page record (sku3) blockNote; Technical Annex v3, sheet 4.

## Slide 8
07 · ARCHITECTURE TARGETS
Every figure here is a target, not a measurement
Architecture targets from the product specification. No SKU-3 silicon has been measured.
DEEPGRID SEMI · SKU-3 HI-REL PMIC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
08
PARAMETER
ARCHITECTURE TARGET
STATUS
Process
180 nm BCD (SCL Mohali production); 130 nm 20 V devices for prototyping
TARGET
Input
4.5 to 40 V continuous; 28 V nominal; 80 V surge; 100 V spike
TARGET
Pre-regulator
Synchronous buck, peak current mode, 500 kHz to 2 MHz
TARGET
Rails
5 V 2 A, 3.3 V 3 A, 1.8 V 500 mA, 1.2/0.9 V 300 mA
TARGET
Reference
Curvature-corrected bandgap, 12 ppm/°C, −55 to +125 °C
TARGET
Telemetry
10-bit 500 kSPS ADC over SPI
TARGET
Upset hardening
DICE latches, TMR sequencer
TARGET
Designed toward, not certificates held: DO-160 sections 16 and 17 · MIL-STD-704F · MIL-STD-1275D · MIL-STD-461G · MIL-STD-883 Class B
Source: product specification (SKU-3), specs and designed-toward list. Status: prototype on 130 nm, then production at SCL 180 nm.
Notes: Every row is an architecture target from the product specification. None is a datasheet value and none is measured: SKU-3 has no silicon yet. Development status is a prototype on 130 nm 20 V devices, then production at SCL 180 nm.
Standards appear only as design direction. DO-160 sections 16 and 17, MIL-STD-704F, MIL-STD-1275D, MIL-STD-461G and MIL-STD-883 Class B are targets the design is developed toward; no certificate exists for any DeepGrid part.
Where the annex sheet shows different rail, ADC or sequencer values, the product specification values shown here apply (see slide 4 notes).
Sources: product page record (sku3) specs and designedToward; SKU-3 Architecture Guide, "Designed toward"; applications status record (sku3).

## Slide 9
08 · QUESTIONS AN EVALUATOR SHOULD ASK
Four questions decide whether it fits your bus
The design team's own open questions. Each needs data before a design-in decision.
DEEPGRID SEMI · SKU-3 HI-REL PMIC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
09
1
100 V surge withstand
During a 100 V, 50 ms load-dump surge, how does the input stage clamp without thermal runaway in the pass devices?
2
Loop stability
Does the regulator keep more than 60° phase margin and 10 dB gain margin with ceramic or tantalum output capacitors across −55 to +125 °C?
3
Cross-rail noise
How much 3.3 V switching ripple reaches the 1.2 V converter supply through the shared reference?
4
Upset spacing
What layout spacing keeps one heavy-ion strike from flipping two of the three voting bits?
Source: product specification (SKU-3), engineering questions. Pre-silicon: no answer here is a measured result yet.
Notes: These four questions come from the design itself; they are what an evaluator should ask the team to answer with data.
1. Surge: during a 100 V, 50 ms load-dump surge, how does the input stage clamp without thermal runaway in the pass devices?
2. Loop: does the regulator keep more than 60 degrees phase margin and 10 dB gain margin with ceramic or tantalum output capacitors across −55 to +125 °C?
3. Noise: how much 3.3 V switching ripple reaches the 1.2 V converter supply through the shared reference?
4. Upsets: what layout spacing keeps one heavy-ion strike from flipping two of the three voting bits?
Pre-silicon, none of these has a measured answer yet; that is exactly why they belong in the evaluation.
Sources: product page record (sku3) questions.

## Slide 10
09 · SUMMARY AND NEXT STEP
Test it against your bus profile before silicon
SKU-3 is an architecture with stated targets; your bus and rail list are the fastest way to test it.
DEEPGRID SEMI · SKU-3 HI-REL PMIC · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
10
WHAT TO TAKE AWAY
One 180 nm BCD die: input conditioning, a peak-current-mode pre-regulator, four monitored rails, a hardened sequencer.
Targets: 4.5 to 40 V in with 80 V surges; 5 V, 3.3 V, 1.8 V and 1.2/0.9 V rails.
Pre-silicon: prototype on 130 nm, production planned at SCL 180 nm. Nothing is measured yet.
1
Share your bus and loads
Input profile, surge cases, rail currents and the start-up order your unit needs.
2
Put the four questions
Surge clamp, loop margin, cross-rail noise and upset spacing, answered with the design team.
3
Scope an evaluation
Check the architecture targets against your unit and agree what the prototype must show.
NEXT STEP · EVALUATION PATH
Start an evaluation: group@deepgrid.in · send your bus profile and rail list
Notes: Close on the action. SKU-3 is one die that conditions a 28 V bus, pre-regulates under peak-current-mode control, produces four monitored rails and sequences them with an upset-hardened state machine. All figures are architecture targets; the part is pre-silicon, with a prototype planned on 130 nm 20 V devices and production at SCL 180 nm.
The ask: send your bus profile and rail list to group@deepgrid.in. The evaluation starts by checking the slide 8 targets against your unit and putting the four questions from slide 9 to the design team.
Sources: product page record (sku3); applications status record (sku3); company contact page (group@deepgrid.in).