## Slide 1
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · RS-485 + CAN-FD · SYSTEM ARCHITECTURE
Two bus links on one die,
protected at every pin
One RS-485 and one CAN-FD line driver on 130 nm with 5 V thick-oxide LDMOS outputs.
20 / 50 ns
DRIVER / RECEIVER DELAY
70 ns loop delay, fixed budget
±15 kV
ESD PROTECTION TARGET
Rated per test standard, not combined
< 8 µA
STANDBY
Local 3.3 V LDO from the 5 V bus
STATUS
Pre-silicon. Every figure in this deck is an architecture target, not a measurement. Evidence today is the architecture sheet; the die is planned for the Cycle-2 wafer run.
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
01
Notes: SKU-5 is a dual-channel line transceiver: one RS-485 channel and one CAN-FD channel on one 130 nm die with 5 V thick-oxide LDMOS outputs.
Headline and subline: product page SKU-5, headline and lede. Figures: product page specs (Timing: 20 ns driver, 50 ns receiver, 70 ns loop delay; Protection target: ±15 kV, stated per test standard; Standby: under 8 µA) and blocks (Local supply: 3.3 V LDO and bandgap from the 5 V bus).
Status: the site's applications record for SKU-5 (status "Cycle-2 wafer run"; evidence "Architecture sheet").
Say plainly: pre-silicon. Every value is a design target (architecture guide, scope note). The ESD figure is not one combined rating: IEC 61000-4-2 and HBM are rated separately (product page reconcile).

## Slide 2
Two line drivers on one die, analog where it counts
An RS-485 channel and a CAN-FD channel, sharing one block set and one 5 V thick-oxide process.
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
02
01 · WHAT IT IS
RS-485 channel
Half duplex, up to 256 nodes, with a common-mode range of −7 to +12 V. A 1.8 V logic interface drives a slew-shaped pre-driver and a differential push-pull output.
A / B · TXD · RXD · EN/STB
CAN-FD channel
An 8 Mbps data phase, designed toward ISO 11898-2, with ±12 V common mode as drawn. Same block set, plus a transmit timeout and bus-fault detection.
CANH / CANL · TXD timeout
Protection and supply
ESD structures on A/B and CANH/CANL, thermal and short-circuit shutdown at 150 °C, and a 3.3 V LDO with bandgap and 40 MHz reference fed from the 5 V bus.
ESD + EMC · Fault · LDO
WHAT IT REPLACES
TI, ADI and Renesas interface parts facing obsolescence: the part a board redesign is forced around.
WHAT SKU-5 IS BUILT ON
Every differentiating block is analog: output devices, receivers, bias and ESD. The logic is a thin skin.
Evidence today: the architecture sheet. Pre-silicon; no figure in this deck is a silicon measurement.
Notes: Two line drivers, one die.
Cards: product page SKU-5, blocks (Logic interface; Driver; Receiver; Protection; Local supply) and specs (RS-485; CAN-FD; Common mode). Guide, Architecture Overview items 1 and 3 (channel titles).
CAN-FD: ISO 11898-2 is a standard the design is developed toward, not one it holds (product page designedToward).
"What it replaces": the site's applications record for SKU-5 ("TI, ADI and Renesas interface parts facing obsolescence"). The "forced around" phrase is a reading of obsolescence, not a sourced figure.
"Analog" line: product page lede ("Every differentiating block is analog; the logic is a thin skin").

## Slide 3
Three bus hazards dictate the silicon
The hazard on the left, the consequence in silicon in the middle, and the blocks that carry it.
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
03
02 · WHY ITS OWN SILICON
THE BUS REQUIRES
SO THE SILICON NEEDS
WHERE IT LANDS
Bus pins face miswiring, ground shifts and electrostatic discharge.
Thick-oxide 5 V LDMOS outputs and large ESD structures, which mature 130 nm offers and advanced nodes do not.
Driver + protection
Output stage · ESD + EMC
Reach and node count depend on edge timing, not headline bit rate.
Trimmed slew control and a fixed propagation budget: 20 ns driver, 50 ns receiver.
Pre-driver + receiver
Slew 3 V/ns trimmed · 50 ns
A dead or open bus must read as a known state.
Failsafe bias holds idle as recessive, with open, short and idle detection.
Receiver
Failsafe bias · bus-state detect
A 5 V-tolerant thick-oxide ring is why 130 nm suits a line driver.
Notes: The bus physics forces the architecture.
Requirement and consequence rows: product page SKU-5, physics (all three pairs, verbatim).
"Where it lands": product page blocks (Driver; Receiver; Protection) and the architecture guide, Component: Channel 1 (Pre-driver dV/dt 3 V/ns trimmed; Receiver 50 ns prop; Failsafe bias).
Closing line: architecture guide, Component: Channel 1, "Why it exists" ("A 5 V-tolerant thick-oxide ring is why 130 nm suits a line driver").

## Slide 4
Two channels mirror each other across the bus pins
Each channel has its own logic interface, driver, receiver, protection, supply and clock.
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
04
03 · SYSTEM ARCHITECTURE
CHANNEL 1 · RS-485
half duplex · up to 256 nodes · −7 to +12 V CM
Logic IF
1.8 V core · level shift to 5 V · TXD · RXD · EN/STB
Pre-driver
slew shaping · dV/dt 3 V/ns trimmed
Output stage
diff push-pull · thick-oxide 5 V LDMOS
Prot logic
EN interlock · no bus contention
Fault
thermal + short · 150 °C shutdown
Receiver
hysteresis comp · 30 mV hyst · 50 ns prop
Failsafe bias
idle = recessive · open / short / idle
ESD + EMC
±15 kV, rated per test standard
Local supply + osc
3.3 V LDO + bandgap · 40 MHz ref
CHANNEL 2 · CAN-FD
8 Mbps data · ISO 11898-2 · ±12 V CM
Local supply + osc
3.3 V LDO + bandgap · 40 MHz · bit-time recovery
ESD + EMC
±15 kV, rated per test standard
Failsafe bias
idle = recessive · open / short / idle
Output stage
diff push-pull · thick-oxide 5 V LDMOS
Pre-driver
slew shaping · dV/dt 3 V/ns trimmed
Logic IF
1.8 V core · level shift to 5 V · TXD · RXD · EN/STB
Receiver
hysteresis comp · 30 mV hyst · 50 ns prop
Fault
thermal + short · 150 °C shutdown
Prot logic
TXD timeout · bus-fault detect
BUS PINS
A / B
RS-485
CANH / CANL
CAN-FD
1
2
3
4
1
TXD enters the logic interface and is level-shifted to 5 V.
2
The pre-driver shapes the edge for the output stage.
3
The differential output drives the A and B pins.
4
The receiver reads the bus back to RXD. Channel 2 follows the same path.
Notes: Read channel 1 left to right: markers 1 to 4 trace one transmit and receive, TXD to the A and B pins and back to RXD. Channel 2 (gray arrows) is the same path, mirrored onto CANH and CANL.
Structure: redrawn from the Technical Annex v3, sheet 6, through the site's diagram spec for SKU-5 (zones, blocks in their spec order, edges and markers).
Values: product page SKU-5 and the SKU-5 architecture guide (Architecture Overview; Components; Key Data Flows 1 to 4).
Bus figures use the corrected forms (product page reconcile): RS-485 common mode −7 to +12 V per TIA/EIA-485, not the sheet's ±7 V; ESD ±15 kV rated per test standard, not "IEC 61000-4-2 ±15 kV HBM". CAN ±12 V is as drawn on the sheet.
Zone colours: blue channel 1, grey bus pins, teal channel 2; cyan is the traced path. Every value is a design target.

## Slide 5
Four block groups, repeated in both channels
What each group does and why it is there, with the blocks that carry it.
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
05
04 · INSIDE THE PART
BLOCK GROUP 1
Logic interface + driver
A 1.8 V core, level-shifted to 5 V, takes TXD, RXD, enable and standby. A pre-driver trimmed to 3 V/ns feeds a push-pull LDMOS output. Why: edge timing sets reach.
Logic IF · Pre-driver 3 V/ns · Output stage 5 V LDMOS
BLOCK GROUP 2
Receiver + failsafe
A 30 mV hysteresis comparator reads the bus back to RXD in 50 ns. Failsafe bias holds idle recessive and detects open, short and idle. Why: a dead bus must read as a known state.
Receiver 30 mV, 50 ns · Failsafe bias
BLOCK GROUP 3
Protection
Thermal and short-circuit shutdown at 150 °C and ESD structures on A/B and CANH/CANL. RS-485 adds an enable interlock, CAN-FD a transmit timeout. Why: these pins leave the board.
Fault 150 °C · ESD + EMC · Prot logic
BLOCK GROUP 4
Local supply + clock
A 3.3 V LDO and bandgap from the 5 V bus, a 1.8 V core rail, and a 40 MHz reference. On CAN-FD the oscillator also serves bit-time recovery.
3.3 V LDO + bandgap · 1.8 V core · 40 MHz
Notes: Four block groups, one job each, repeated per channel.
Text: product page SKU-5, blocks (Logic interface; Driver; Receiver; Protection; Local supply) and physics (the "Why" lines).
Block detail: SKU-5 architecture guide, Component: Channel 1 and Component: Channel 2 (Prot logic: EN interlock, no bus contention; TXD timeout, bus-fault detect; Local supply + osc: 40 MHz, bit-time recovery on channel 2).
All values are architecture targets from the Technical Annex v3, sheet 6, as carried by the product page.

## Slide 6
Four decisions, and the check that tests each
Each choice, the alternative it rules out, the reason, and the check an evaluator should run.
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
06
05 · DESIGN DECISIONS
DECISION
INSTEAD OF
WHY
WHAT TO VERIFY
Thick-oxide 5 V LDMOS outputs and large ESD structures on mature 130 nm
An advanced, thin-oxide node
Bus pins face miswiring, ground shifts and electrostatic discharge; advanced nodes do not offer these devices.
Which ESD structures have silicon data at ±15 kV. That needs a dedicated test chip.
Trimmed slew at 3 V/ns and a fixed 20 ns / 50 ns timing budget
Chasing a headline bit rate
Reach and node count depend on edge timing: 20 Mbps over short runs, about 83 kbps at 1.2 km.
Whether 256 nodes are reached with eighth-unit-load receivers, and at what input impedance.
Failsafe bias that holds idle as recessive
An undefined receiver output on a dead bus
A dead or open bus must read as a known state, with open, short and idle detected.
RXD state and the detection flags with the bus open, shorted and idle.
Two channels on one shared block set
A separate RS-485 part and CAN part
Logic in, shaped and driven onto the bus, received back, with protection around every pin.
Which discontinued interface part is the first drop-in replacement.
Rows 1, 2 and 4 carry the three evaluator questions on slide 9; row 3 is a bench check that follows from the failsafe requirement.
Notes: Four decisions, each with a check.
Row 1: product page physics 1; question "ESD on an open process".
Row 2: product page physics 2 and specs (RS-485: 20 Mbps over short runs, about 83 kbps at 1.2 km; Timing); guide, Pre-driver (dV/dt 3 V/ns trimmed); question "Unit load".
Row 3: product page physics 3 and blocks (Receiver: failsafe bias and bus-state detection). The verify cell is a reading of that requirement, not a product-page question.
Row 4: product page lede and blockNote ("Two channels share one block set..."); question "First pin-compatible target".
The "Instead of" column names the alternative each decision rules out; it is a reading of the sources, not a measured comparison.

## Slide 7
One bit takes four steps from TXD back to RXD
The transmit and receive path, numbered as on the diagram, with its timing budget and fault states.
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
07
06 · KEY DATA FLOW
1
Shift
TXD enters the logic interface and is level-shifted from the 1.8 V core to 5 V.
2
Shape
The pre-driver shapes the edge, slew trimmed to 3 V/ns, for the output stage.
3
Drive
The differential push-pull output drives A and B: 20 ns driver delay.
4
Read back
The 30 mV hysteresis receiver reads the bus back to RXD: 50 ns.
A 70 ns loop-delay budget
Driver 20 ns plus receiver 50 ns gives a 70 ns loop delay. Reach and node count follow that budget, so RS-485 is stated as two operating points: 20 Mbps over short runs, about 83 kbps at 1.2 km.
Steps 3 and 4 · channel 2 follows the same path
When the bus is dead or faulted
Failsafe bias holds idle as recessive and flags open, short and idle. Thermal and short-circuit shutdown acts at 150 °C; RS-485 has an enable interlock against contention, CAN-FD a transmit timeout.
Receiver, Failsafe bias, Fault, Prot logic
Notes: One bit, four steps; then the timing budget and what happens on a dead or faulted bus.
Steps 1 to 4: SKU-5 architecture guide, Key Data Flows; the same markers as the system diagram (diagram spec for SKU-5, markers). Step detail: product page blocks (Logic interface; Driver; Receiver) and guide, Component: Channel 1.
Timing card: product page specs (Timing: 20 ns driver, 50 ns receiver; 70 ns loop delay; RS-485 rate and reach) and physics 2. Rate and reach are two operating points, not one (product page reconcile; the annex sheet paired 20 Mbps with 1.2 km).
Fault card: product page physics 3 and blocks (Protection); guide, Prot logic (EN interlock, no bus contention; TXD timeout, bus-fault detect).

## Slide 8
Every figure here is a target, not a measurement
Seven rows from the product page specification, each one labelled a target, with the annex corrections.
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
08
07 · ARCHITECTURE TARGETS
PARAMETER
ARCHITECTURE TARGET
STATUS
Process
130 nm with 5 V thick-oxide LDMOS
Target
RS-485
Half duplex, up to 256 nodes; 20 Mbps over short runs, about 83 kbps at 1.2 km
Target
CAN-FD
8 Mbps data phase, ISO 11898-2
Target
Common mode
RS-485 −7 to +12 V (TIA/EIA-485); CAN ±12 V as drawn
Target
Timing
20 ns driver, 50 ns receiver; 70 ns loop delay
Target
Protection target
±15 kV, stated per test standard
Target
Standby
Under 8 µA
Target
Designed toward
TIA/EIA-485; ISO 11898-2; IEC 61000-4-2 (system level) and HBM (component level), rated separately. Targets, not certificates.
Corrected from the annex sheet
The sheet paired 20 Mbps with 1.2 km and quoted ±7 V and "IEC 61000-4-2 ±15 kV HBM". This deck: two operating points, −7 to +12 V, and two ESD tests rated apart.
Evidence today
Pre-silicon. The architecture sheet; the die is planned for the Cycle-2 wafer run.
Notes: Targets, not measurements.
Table: product page SKU-5, specs (all seven rows, verbatim values).
Designed toward: product page designedToward; architecture guide, Designed toward and scope note ("no certificate exists for any DeepGrid part"). ISO 11898-2 and TIA/EIA-485 in the table name the standard each figure is drawn against; neither is held.
Corrected from the annex sheet: product page reconcile, which states that rate and reach are two operating points, IEC 61000-4-2 and HBM are different tests, and TIA/EIA-485 specifies −7 to +12 V.
Evidence today: the site's applications record for SKU-5 (status "Cycle-2 wafer run"; evidence "Architecture sheet").

## Slide 9
Three questions decide whether SKU-5 fits your bus
Put these to DeepGrid before committing bench time. Each tests one part of the architecture.
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
09
08 · EVALUATOR QUESTIONS
ESD on an open process
Which ESD structures have silicon data at ±15 kV? This needs a dedicated test chip; it cannot be inferred from shared tiles.
Tests the ESD + EMC blocks on A/B and CANH/CANL
1
Unit load
Are 256 nodes reached with eighth-unit-load receivers, and at what input impedance?
Tests the RS-485 receiver and the node-count target
2
First pin-compatible target
Which discontinued interface part is the first drop-in replacement?
Tests the pinout and package plan
3
The architecture sheet asks these of itself. Each needs silicon, a test chip or a dated plan.
Notes: Three questions, verbatim from the product page SKU-5, questions (titles and wording unchanged).
The "Tests" line maps each question to the blocks on slides 4 and 5 that must answer it; the pinout mapping for question 3 is a reading of "drop-in replacement".
"Each needs silicon, a test chip or a dated plan to settle" follows from the pre-silicon status (architecture guide scope note) and question 1's own wording.

## Slide 10
09 · NEXT STEP
Test it against your cable, node count and ESD
Bring three things to the first call: your cable length and data rate, your node count and receiver unit load, and the ESD test and level your system must meet.
DISCUSS THIS PART
group@deepgrid.in
Subject: SKU-5 interface transceiver
WHAT TO TAKE AWAY
Drives
Thick-oxide 5 V LDMOS outputs with slew trimmed to 3 V/ns, in a 20 ns driver budget.
Reads
A 30 mV hysteresis receiver at 50 ns, with failsafe bias holding a dead bus recessive.
Protects
ESD structures on every bus pin, ±15 kV targeted per test standard, and 150 °C shutdown.
Status
Pre-silicon, planned for the Cycle-2 wafer run. Every figure is an architecture target.
DEEPGRID SEMI · SKU-5 INTERFACE TRANSCEIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
10
Notes: One action: evaluate SKU-5 against the bus's cable length, node count and ESD requirement.
Contact: the site's contact page addresses group@deepgrid.in; the product page "Discuss this part" button carries the part name.
Summary lines: product page SKU-5 (physics, blocks, specs, designedToward); status: the site's applications record for SKU-5.
Do not imply a datasheet, a certificate or a delivery date; none exists.