## Slide 1
DEEPGRID SEMI · SKU-6 · QUAD-RAIL VOLTAGE SUPERVISOR
Watch four rails, ignore the noise, latch the fault
Architecture targets for a supervisor on 130 nm CMOS (prototype) and 180 nm (production): chopper-stabilised comparators, matched dividers, an 8 µs deglitch, a latched fault and a windowed watchdog. Planned as the first part through the MIL-STD-883 screening flow.
PRE-SILICON · EVERY FIGURE IS A DESIGN TARGET, NOT A MEASUREMENT
4 rails
SUPERVISED INPUTS
5.0, 3.3, 1.8 and 1.2/0.9 V adjustable
<500 µV
COMPARATOR OFFSET
Chopper-stabilised, on 0.1%-matched dividers
8 µs
DIGITAL DEGLITCH
Converter ripple ignored; a real brownout latched
10 ppm/°C
REFERENCE DRIFT
Curvature-corrected bandgap, OTP trim
DEEPGRID SEMI · SKU-6 QUAD-RAIL VOLTAGE SUPERVISOR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
01
Notes: SKU-6 is DeepGrid's quad-rail voltage supervisor. It watches four supply rails and the processor that depends on them, ignores converter switching noise with an 8 µs deglitch, and latches a fault the system cannot ignore.
Say plainly: this is pre-silicon. Development status is a cycle-1 or cycle-2 wafer run, prototype on 130 nm CMOS and production on 180 nm. The strongest evidence today is that the sensing chain's digital logic has run as circuit code on an FPGA; the analog comparators and the bandgap cannot be proven that way, and no silicon has been measured. Every number in this deck is an architecture target.
SKU-6 is planned as the first DeepGrid part through the MIL-STD-883 screening flow. That is a plan and a design direction, not a qualification held.
Sources: product page record (sku6) headline, lede and specs; SKU-6 Architecture Guide, "What is SKU-6?"; applications status record (sku6); Technical Annex v3, sheet 7.

## Slide 2
01 · WHAT IT IS
One part watches four rails and the processor
SKU-6 senses each rail, decides whether a crossing is a real fault, and tells the system it happened.
DEEPGRID SEMI · SKU-6 QUAD-RAIL VOLTAGE SUPERVISOR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
02
Sense four rails
Each rail runs through its own 0.1%-matched divider, a chopper-stabilised comparator with offset under 500 µV, and an 8 µs deglitch counter.
Decide and latch
One maskable fault matrix collects the four chains, latches a confirmed fault and holds it in registers the processor can read over I²C.
Signal and time
FAULT_N asserts first, then RESET_N with a 200 ms delay. A windowed watchdog, 100 ms to 1.6 s, resets a hung or runaway processor.
THE FOUR SUPERVISED RAILS · ARCHITECTURE TARGETS
5.0 V
RAIL 1 · ±1% THRESHOLD
3.3 V
RAIL 2 · ±1% THRESHOLD
1.8 V
RAIL 3 · ±2% THRESHOLD
1.2/0.9 V
RAIL 4 · ADJUSTABLE · ±2%
Source: product specification (SKU-6); SKU-6 Architecture Guide, sense chain. Pre-silicon design targets.
Notes: Three jobs sit in one part. It senses: each of four rails goes through an ESD-protected input, a 0.1%-matched polysilicon divider, a chopper-stabilised comparator with offset under 500 µV and 8 mV hysteresis, and an 8 µs digital deglitch counter. It decides: a maskable, latched fault matrix with a priority encoder, mask register and I²C registers. It signals and times: open-drain FAULT_N asserts before open-drain RESET_N, which has a trimmed 200 ms delay; there is a manual-reset input; and a windowed watchdog adjustable from 100 ms to 1.6 s catches a hung or runaway processor.
Rails are 5.0, 3.3, 1.8 and 1.2 or 0.9 V adjustable (product specification). The guide's comparator accuracy is plus or minus 1% on the two upper rails and plus or minus 2% on the two lower ones.
Sources: product page record (sku6) lede, blocks and specs; SKU-6 Architecture Guide, "What is SKU-6?" and "Architecture Overview" items 1 to 5.

## Slide 3
02 · WHY IT NEEDS ITS OWN SILICON
Accuracy and noise immunity set the silicon
Three requirements of a supervisor each force one silicon choice.
DEEPGRID SEMI · SKU-6 QUAD-RAIL VOLTAGE SUPERVISOR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
03
REQUIREMENT
SILICON CONSEQUENCE
THRESHOLD ACCURACY
Thresholds accurate to a fraction of a percent.
Comparators with offset under 500 µV and 0.1%-matched polysilicon dividers, trimmed once.
NOISE IMMUNITY
A buck converter’s ripple must not trip it; a real brownout must.
An 8 µs digital deglitch window between the comparator and the latch.
REFERENCE STABILITY
A reference stable over the military temperature range.
A curvature-corrected bandgap at 10 ppm/°C.
Source: product specification (SKU-6), physical requirements. Pre-silicon design targets.
Notes: This is why a supervisor earns its own die rather than a comparator and a timer from the parts bin. Each requirement forces one choice.
Threshold accuracy: thresholds accurate to a fraction of a percent need comparators with offset under 500 µV, which is why they are chopper-stabilised, and 0.1%-matched polysilicon dividers, trimmed once.
Noise immunity: a buck converter's ripple must not trip a reset, but a real brownout must. That is the 8 µs digital deglitch window between the comparator and the latch. The guide calls the deglitch counter the part that does both jobs.
Reference stability: a reference stable over the military temperature range needs a curvature-corrected bandgap at 10 ppm/°C. The guide notes the bandgap and trimmed polysilicon resistors are what make the threshold accuracy possible on a mature node.
Sources: product page record (sku6) physics; SKU-6 Architecture Guide, sense chain and reference sections; Technical Annex v3, sheet 7.

## Slide 4
03 · SYSTEM ARCHITECTURE
Every rail fault ends at one latch and one reset
Four sense chains feed one latched fault matrix; the reference sets every threshold at 4.
DEEPGRID SEMI · SKU-6 QUAD-RAIL VOLTAGE SUPERVISOR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
04
SENSE CHAIN · ONE PER RAIL
VIN 1
5.0 V · ESD 2 kV
Divider
poly · 0.1% match
Comparator
chopper · ±1%
Deglitch
8 µs counter
VIN 2
3.3 V · ESD 2 kV
Divider
poly · 0.1% match
Comparator
chopper · ±1%
Deglitch
8 µs counter
VIN 3
1.8 V · ESD 2 kV
Divider
poly · 0.1% match
Comparator
chopper · ±2%
Deglitch
8 µs counter
VIN 4
1.2/0.9 V · ESD 2 kV
Divider
poly · 0.1% match
Comparator
chopper · ±2%
Deglitch
8 µs counter
FAULT LOGIC
Fault matrix
maskable · latched · priority encoder · mask register · I²C registers
OUTPUT STAGE
RESET_N
open-drain · 200 ms delay
FAULT_N
asserts before RESET_N
MR
manual reset in
REFERENCE + TIMEBASE
Bandgap
1.20 V · 10 ppm/°C
Trim
OTP 5-bit · ±0.5%
Oscillator
1 MHz timebase
WATCHDOG
Window logic
100 ms to 1.6 s
WDI
kick input
Timeout
counter to RESET_N
READING PATH
Each rail enters through its divider.
The comparator and deglitch counter report a confirmed fault to the matrix.
The matrix latches it and drives FAULT_N, then RESET_N.
The trimmed bandgap sets every comparator threshold.
A missed or early watchdog kick times out to RESET_N.
A spike shorter than 8 µs never reaches the latch.
1
2
3
4
5
1
2
3
4
5
Redrawn from Technical Annex v3, sheet 7. Watchdog range, rail 4 and oscillator follow the product specification. All values are design targets.
Notes: Read it by the numbers. 1: each rail enters through its divider. 2: the comparator and deglitch counter report a confirmed fault to the matrix. 3: the matrix latches it and drives FAULT_N, then RESET_N. 4: the trimmed bandgap sets every comparator threshold. 5: a missed or early watchdog kick times out to RESET_N.
Every path ends at the same place: one latched fault and one delayed reset. The deglitch counter is the reason a converter spike shorter than 8 µs never reaches the latch.
Where this differs from the annex sheet: structure follows sheet 7, but some values differ and this deck follows the product specification. The sheet shows the watchdog window as 1 ms / 10 ms; the product specification states adjustable 100 ms to 1.6 s. The sheet and the guide label rail 4 as 1V2; the product specification states 1.2 or 0.9 V adjustable. The guide and the sheet show an 8 MHz RC oscillator (plus or minus 2%, deglitch "8 µs at 8 MHz"); the product specification blocks state a 1 MHz oscillator, which is what is drawn here. Confirm the clock with the design team.
Sources: SKU-6 Architecture Guide, "Architecture Overview" and "Key Data Flows"; diagram spec scripts/sku-diagrams/specs.py (sku6); Technical Annex v3, sheet 7.

## Slide 5
04 · COMPONENTS
Each block protects threshold accuracy or timing
Four blocks, colour-keyed to the architecture diagram; each one exists for a specific reason.
DEEPGRID SEMI · SKU-6 QUAD-RAIL VOLTAGE SUPERVISOR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
05
Sense chain, one per rail
Accuracy and noise immunity: ripple must not trip a reset, a real fault must still be caught.
ESD-protected input, 2 kV; 0.1%-matched polysilicon divider; chopper-stabilised comparator, offset under 500 µV, ±1% or ±2%, 8 mV hysteresis; 8 µs digital deglitch counter.
Fault logic and outputs
Timing: a confirmed fault is latched and announced before the board resets.
Maskable fault matrix with priority encoder, mask register, latch and I²C registers. Open-drain FAULT_N asserts before open-drain RESET_N, 200 ms trimmed delay; manual-reset input.
Reference and timebase
Accuracy: the bandgap and trimmed resistors make the thresholds possible on a mature node.
Curvature-corrected bandgap, 1.20 V, 10 ppm/°C, PTAT + CTAT; one-time-programmable 5-bit trim to ±0.5%; 1 MHz oscillator with reference current.
Watchdog
Timing: catches a processor that has hung or is running away.
Windowed timer adjustable from 100 ms to 1.6 s with open and close windows; WDI kick input; timeout counter drives RESET_N.
Source: SKU-6 Architecture Guide, component sections; product specification (SKU-6). Pre-silicon design targets.
Notes: Two of these blocks exist for accuracy, two for timing.
Sense chain: switching noise must not trip a reset, yet a real fault must still be caught quickly; the deglitch counter does both. Each rail: ESD-protected input at 2 kV, 0.1%-matched polysilicon divider, chopper-stabilised comparator (plus or minus 1% on 5.0 and 3.3 V, plus or minus 2% on 1.8 and 1.2 V, 8 mV hysteresis), 8 µs digital deglitch counter.
Fault logic and outputs: the maskable fault matrix latches a confirmed fault; FAULT_N asserts before RESET_N so the system knows why it is about to reset. RESET_N has a trimmed 200 ms delay. The "announced before the board resets" phrasing is our reading of that ordering.
Reference and timebase: the bandgap and trimmed polysilicon resistors are what make the threshold accuracy possible on a mature node. 1.20 V, 10 ppm/°C, 5-bit OTP trim to plus or minus 0.5%. Oscillator: the product specification states 1 MHz; the guide states an 8 MHz RC oscillator at plus or minus 2% over −40 to 125 °C. This deck follows the product specification.
Watchdog: windowed, adjustable 100 ms to 1.6 s (product specification; the annex sheet shows 1 ms / 10 ms). A kick that is missed or arrives too early times out to RESET_N.
Sources: SKU-6 Architecture Guide, "Component" sections; product page record (sku6) blocks and specs.

## Slide 6
05 · DESIGN DECISIONS
Each choice buys accuracy or immunity at a cost
Five architecture choices, what each protects against, and what it asks of the design or the board.
DEEPGRID SEMI · SKU-6 QUAD-RAIL VOLTAGE SUPERVISOR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
06
DECISION
WHAT IT BUYS
WHAT IT COSTS
Chopper-stabilised comparators
Offset under 500 µV, so the threshold holds to a fraction of a percent.
The chopper adds its own ripple, which must be filtered before the fault latch.
0.1%-matched poly dividers, OTP trim
Divider ratios matched to 0.1%; the 5-bit trim reaches ±0.5% after trim.
Trim is one-time; polysilicon drift over twenty years at high temperature is still open.
8 µs digital deglitch
Converter ripple shorter than the window never trips a reset.
Every real fault waits 8 µs before it latches; the window must still beat memory corruption.
Latched fault, FAULT_N before RESET_N
A fault the system cannot ignore, with its cause held in readable registers.
A latched fault stays set until it is cleared, so system firmware must handle the clear.
Windowed watchdog, 100 ms to 1.6 s
Catches a processor that hangs and one that runs away and kicks too early.
Firmware must kick inside the window, not merely often enough.
Source: product specification (SKU-6), physics, specs and questions; SKU-6 Architecture Guide. Costs follow from the named mechanism.
Notes: Every choice buys accuracy or noise immunity and asks something in return; the costs are what to probe in evaluation.
Comparators: chopper stabilisation gets offset under 500 µV, but the chopper creates its own ripple; the design team's own question is what filtering removes it before the fault latch.
Dividers: 0.1%-matched polysilicon with a 5-bit one-time trim to plus or minus 0.5%. The open question is how far polysilicon drift moves the 0.1% ratio over twenty years at high temperature.
Deglitch: 8 µs rejects converter ripple, but it also delays every real fault by up to that window. Whether 8 µs is short enough to stop memory corruption before reset is the first evaluator question.
Latching: FAULT_N asserts before RESET_N and the cause is held in I²C registers; a latched fault needs an explicit clear, which system firmware must own.
Watchdog: windowed means an early kick is a fault too, which catches a runaway processor as well as a hung one.
The "what it costs" column is a fair reading of each named mechanism, not a measured penalty.
Sources: product page record (sku6) physics, specs and questions; SKU-6 Architecture Guide, component sections.

## Slide 7
06 · KEY DATA FLOW
Five steps take a rail fault to a held reset
Steps 1 to 3 carry a rail fault; step 4 sets the thresholds; step 5 is the watchdog path to reset.
DEEPGRID SEMI · SKU-6 QUAD-RAIL VOLTAGE SUPERVISOR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
07
1
Rail in
Each rail enters through its divider.
2
Confirmed
The comparator and deglitch counter report a confirmed fault to the matrix.
3
Latched
The matrix latches it and drives FAULT_N, then RESET_N.
4
Threshold
The trimmed bandgap sets every comparator threshold.
5
Watchdog
A missed or early watchdog kick times out to RESET_N.
SUPPORTING PATHS INTO THE SAME LATCH AND RESET
What the board sees
FAULT_N asserts first, so the system knows why; RESET_N follows and holds for 200 ms after the fault.
What never reaches the latch
A converter spike shorter than the 8 µs deglitch window is filtered before the fault matrix sees it.
Source: SKU-6 Architecture Guide, "Key Data Flows" markers 1 to 5; product specification block note.
Notes: Walk the five steps. 1: each rail enters through its divider. 2: the comparator and deglitch counter report a confirmed fault to the matrix. 3: the matrix latches it and drives FAULT_N, then RESET_N. 4: the trimmed bandgap sets every comparator threshold. 5: a missed or early watchdog kick times out to RESET_N.
Steps 1 to 3 are the fault sequence; step 4 is the reference that makes every threshold accurate; step 5 is the second way to reach reset, through the processor's timing rather than a rail.
For a board designer: FAULT_N comes before RESET_N, RESET_N is delayed 200 ms, and a spike shorter than 8 µs is filtered out before the matrix.
Sources: SKU-6 Architecture Guide, "Key Data Flows" and output stage; product page record (sku6) blockNote; Technical Annex v3, sheet 7.

## Slide 8
07 · ARCHITECTURE TARGETS
Every figure here is a target, not a measurement
Architecture targets from the product specification. No SKU-6 silicon has been measured.
DEEPGRID SEMI · SKU-6 QUAD-RAIL VOLTAGE SUPERVISOR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
08
PARAMETER
ARCHITECTURE TARGET
STATUS
Process
130 nm CMOS prototype, 180 nm production
TARGET
Rails
5.0, 3.3, 1.8 and 1.2/0.9 V adjustable
TARGET
Comparator offset
Under 500 µV, chopper stabilised
TARGET
Threshold network
0.1%-matched polysilicon, OTP trim
TARGET
Deglitch
8 µs digital filter
TARGET
Reference
10 ppm/°C bandgap
TARGET
Watchdog
Windowed, 100 ms to 1.6 s
TARGET
Outputs
Latched FAULT_N, RESET_N after 200 ms
TARGET
Designed toward, not a certificate held: MIL-STD-883K Class B screening flow. SKU-6 is planned as the first DeepGrid part through it.
Source: product specification (SKU-6), specs and designed-toward list. Status: cycle-1 or cycle-2 wafer run, pre-silicon.
Notes: Every row is an architecture target from the product specification. None is a datasheet value and none is measured: SKU-6 has no silicon yet. Status is a planned cycle-1 or cycle-2 wafer run; the sensing chain's digital logic has run as circuit code on an FPGA.
The standard appears only as design direction. The MIL-STD-883K Class B screening flow is a target the design is developed toward, and SKU-6 is planned as the first part through it; no certificate exists for any DeepGrid part.
Where the annex sheet shows a different watchdog window (1 ms / 10 ms), the product specification value (100 ms to 1.6 s) applies; see slide 4 notes for the other differences.
Sources: product page record (sku6) specs and designedToward; SKU-6 Architecture Guide, "Designed toward"; applications status record (sku6).

## Slide 9
08 · QUESTIONS AN EVALUATOR SHOULD ASK
Four questions decide whether it fits your board
The design team's own open questions. Each needs data before a design-in decision.
DEEPGRID SEMI · SKU-6 QUAD-RAIL VOLTAGE SUPERVISOR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
09
1
Deglitch window
Is 8 µs long enough to ignore converter noise and short enough to stop memory corruption before reset?
2
Chopper ripple
What filtering removes the chopper’s own ripple before the fault latch?
3
Ladder ageing
How far does polysilicon drift move the 0.1% ratio over twenty years at high temperature?
4
Why this part first
What does taking SKU-6 through screening first establish for every part that follows?
Source: product specification (SKU-6), engineering questions. Pre-silicon: no answer here is a measured result yet.
Notes: These four questions come from the design itself; they are what an evaluator should ask the team to answer with data.
1. Deglitch: is 8 µs long enough to ignore converter noise and short enough to stop memory corruption before reset? Bring your converter switching frequencies and your memory's brownout tolerance.
2. Chopper ripple: what filtering removes the chopper's own ripple before the fault latch?
3. Ladder ageing: how far does polysilicon drift move the 0.1% ratio over twenty years at high temperature?
4. Why this part first: what does taking SKU-6 through screening first establish for every part that follows?
Pre-silicon, none of these has a measured answer yet; that is exactly why they belong in the evaluation.
Sources: product page record (sku6) questions.

## Slide 10
09 · SUMMARY AND NEXT STEP
Test it against your rails before silicon
SKU-6 is an architecture with stated targets; your rail list and noise profile are the fastest test.
DEEPGRID SEMI · SKU-6 QUAD-RAIL VOLTAGE SUPERVISOR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
10
WHAT TO TAKE AWAY
Four sense chains, one latched fault matrix, open-drain FAULT_N and RESET_N, a trimmed reference and a windowed watchdog.
Targets: offset under 500 µV, 0.1%-matched dividers, 8 µs deglitch, 10 ppm/°C reference, 100 ms to 1.6 s watchdog.
Pre-silicon: a cycle-1 or cycle-2 wafer run is planned. Nothing is measured yet.
1
Share your rails and timing
Rail voltages and thresholds, converter switching frequencies and the reset delay you need.
2
Put the four questions
Deglitch window, chopper ripple, ladder ageing and the screening plan, answered with the design team.
3
Scope an evaluation
Check the architecture targets against your board and agree what the prototype must show.
NEXT STEP · EVALUATION PATH
Start an evaluation: group@deepgrid.in · send your rail list and converter noise profile
Notes: Close on the action. SKU-6 watches four rails with chopper-stabilised comparators on matched dividers, filters converter noise with an 8 µs deglitch, latches a real fault and announces it on FAULT_N before a 200 ms RESET_N, and runs a windowed watchdog on the processor. All figures are architecture targets; the part is pre-silicon, with a cycle-1 or cycle-2 wafer run planned and the MIL-STD-883 screening flow as its design direction.
The ask: send your rail list, converter switching frequencies and reset timing to group@deepgrid.in. The evaluation starts by checking the slide 8 targets against your board and putting the four questions from slide 9 to the design team.
Sources: product page record (sku6); applications status record (sku6); company contact (group@deepgrid.in).