## Slide 1
DEEPGRID SEMI · SKU-7 · 77 GHZ 4D MIMO RADAR
Two dies: SiGe for 77 GHz, CMOS for the math
Architecture targets for a 76 to 81 GHz FMCW radar: a SiGe front end for the chirp, two transmitters and four receive channels, and a 130 nm CMOS die for conversion, FFTs, detection and tracking.
PRE-SILICON · FIRST IHP WAFER RUN PLANNED FY28 · EVERY FIGURE IS A DESIGN TARGET
77 GHz
OPERATING BAND
4 GHz chirp sweep inside 76 to 81 GHz
3.75 cm
RANGE RESOLUTION
Set by the 4 GHz sweep
2TX / 4RX
MIMO ARRAY
Two 13 dBm transmitters, four receive channels
64
TRACKED TARGETS
Range, velocity, angle and RCS per frame
DEEPGRID SEMI · SKU-7 77 GHZ MIMO RADAR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
01
Notes: SKU-7 is DeepGrid's 77 GHz 4D imaging radar, split across two dies: a silicon-germanium transceiver for the 77 GHz front end and a 130 nm CMOS die for sampling, FFTs and target detection.
Say plainly: this is pre-silicon. The status record reads "IHP wafer run, FY28". The sheet's own risk statement applies: the SiGe front end has no FPGA equivalent, so it is proven on silicon or not at all. Every number in this deck is an architecture target, not a measurement.
Sources: product page record (sku7) headline, lede and specs; SKU-7 Architecture Guide, "What is SKU-7?"; applications status record (sku7); Technical Annex v3, sheet 8.

## Slide 2
01 · WHAT IT IS
SiGe sends and receives; CMOS finds targets
SKU-7 is a two-transmit, four-receive FMCW radar for the 76 to 81 GHz band, built from two dies.
DEEPGRID SEMI · SKU-7 77 GHZ MIMO RADAR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
02
Synthesise and transmit
A 40 MHz crystal, a ramp generator and a fractional-N PLL drive a 38.5 GHz SiGe VCO. A doubler reaches 77 GHz and two power amplifiers transmit the chirp.
Receive four echoes
Four identical channels amplify, mix and filter the reflections. The beat frequency carries range; the phase across the four receivers carries angle.
Digitise and detect
Four 12-bit converters sample the IF. Range and Doppler FFTs, CFAR detection and angle estimation turn the samples into a list of tracked targets.
TWO DIES, ONE BOUNDARY · ARCHITECTURE TARGETS
SiGe die
130 nm SiGe BiCMOS (IHP SG13G2), fT above 350 GHz
Chirp synthesis, two PAs, four receive chains
CMOS die
130 nm CMOS at 200 MHz
Four 12-bit 40 MSPS converters, FFTs, CFAR, angle, tracker
IF SIGNALS × 4
cross the package boundary
Source: product specification (SKU-7) and SKU-7 Architecture Guide. Pre-silicon design targets.
Notes: The work divides cleanly between two dies. The SiGe die synthesises the chirp, transmits it on two power amplifiers and mixes the four echoes down to IF. The 130 nm CMOS die digitises the four IF signals, runs range and Doppler FFTs, CFAR detection and angle estimation, and keeps a target list.
Process targets: the front end is 130 nm SiGe BiCMOS on IHP SG13G2 with transistor fT above 350 GHz; the baseband is 130 nm CMOS at 200 MHz. Note that fT is a transistor capability, not the radar's operating frequency.
The only thing that crosses between the dies is the IF from the four receive channels.
Sources: product page record (sku7) lede, blocks, blockNote and specs; SKU-7 Architecture Guide, "What is SKU-7?" and "Architecture Overview".

## Slide 3
02 · WHY IT NEEDS ITS OWN SILICON
77 GHz physics decides where each block sits
Three requirements each force one silicon choice, and together they split the radar across two dies.
DEEPGRID SEMI · SKU-7 77 GHZ MIMO RADAR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
03
REQUIREMENT
SILICON CONSEQUENCE
GAIN AT 77 GHZ
The front end needs transistor gain at 77 GHz.
SiGe heterojunction transistors with transition frequency above 350 GHz; standard CMOS lacks the margin.
RANGE RESOLUTION OF 3.75 CM
Targets 3.75 cm apart must resolve as two returns.
A 4 GHz chirp sweep with a linear, low-noise frequency ramp.
FAST CONVERTERS NEXT TO RF
Fast converters and FFTs must run close to sensitive receivers.
The converters sit on the CMOS die, across a package boundary from the RF.
Source: product specification (SKU-7), physical requirements. Pre-silicon design targets.
Notes: This is why SKU-7 is two dies rather than one. Each requirement forces one choice.
Gain at 77 GHz: SiGe heterojunction transistors with transition frequency above 350 GHz; standard CMOS lacks the margin. The guide adds that only a SiGe HBT reaches 77 GHz on a mature node.
Range resolution of 3.75 cm: that takes a 4 GHz chirp sweep, and the frequency ramp has to be linear and low-noise across it.
Converters next to RF: fast converters and FFTs are noisy neighbours, so they sit on the CMOS die, across a package boundary from the receivers.
The left-hand row text restates each requirement in plain words; the consequences are quoted from the product specification.
Sources: product page record (sku7) physics; SKU-7 Architecture Guide, "Component: Chirp synthesis + transmit", "Why it exists".

## Slide 4
03 · SYSTEM ARCHITECTURE
One chirp goes out; four echoes cross as IF
Transmit and receive sit on the SiGe die; the IF crosses at 4 to the CMOS die, which finds the targets.
DEEPGRID SEMI · SKU-7 77 GHZ MIMO RADAR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
04
SIGE DIE · 130 NM SIGE BICMOS, IHP SG13G2
CMOS DIE · 130 NM CMOS AT 200 MHZ
CHIRP SYNTHESIS + TRANSMIT
XTAL
40 MHz
Ramp gen
sawtooth / triangle
PLL
fractional-N · 1 MHz loop BW
PA · TX1, TX2
13 dBm each
× 2
to 77 GHz · LO out
VCO
38.5 GHz · SiGe HBT
DETECTION + OUTPUT
CFAR
cell-averaging
Angle est
digital beamform · 15°
Target list
range · velocity · angle · RCS · up to 64 tracks
To the ECU
CAN-FD · 100BASE-T1 · MIPI CSI-2
RECEIVE · 4 CHANNELS
LNA × 4
3.5 dB NF
Mixer × 4
LO from the × 2
IF amp × 4
beat frequency
AAF × 4
10 MHz LP
Range and angle
beat frequency carries range; phase across the four receivers carries angle
DIGITISE + TRANSFORM
Range-Doppler map
SRAM 512 KB
Doppler FFT
128-pt across chirps
ADC × 4
12-bit · 40 MSPS
Windowing
Hann / Blackman
Range FFT
1024-pt radix-4 · 26 µs per chirp
LO
READING PATH
The crystal, ramp generator, PLL and VCO synthesise the chirp.
The doubler reaches 77 GHz and the two PAs transmit.
Each of four echoes is amplified, mixed with the LO and filtered.
The IF signals cross to the CMOS die and are digitised.
The range-Doppler map feeds CFAR detection and angle estimation.
The target list goes to the ECU.
1
2
3
4
5
6
1
2
3
4
5
6
Redrawn from Technical Annex v3, sheet 8. Converter placement and ECU interfaces follow the product specification. All values are design targets.
Notes: Read it by the numbers. 1: the crystal, ramp generator, PLL and VCO synthesise the chirp. 2: the doubler reaches 77 GHz and the two PAs transmit. 3: each of four echoes is amplified, mixed with the LO and filtered. 4: the four IF signals cross the die boundary and are digitised at 12 bits, 40 MSPS. 5: the range-Doppler map feeds CFAR detection and angle estimation. 6: the target list goes to the ECU over CAN-FD, 100BASE-T1 or MIPI CSI-2.
The left column is the SiGe die, the right column the CMOS die; the dashed line is the package boundary. The doubler output also serves as the LO for the four mixers.
Where this differs from the guide and the annex sheet: the guide's diagram draws the 12-bit ADCs inside the SiGe receive chain. The product specification places the four converters on the CMOS die with the IF crossing the boundary, and the annex sheet's own text agrees ("ADC is the boundary"); this deck follows the product specification. The sheet names the ECU interfaces as CAN-FD and Ethernet; the product specification states CAN-FD, 100BASE-T1 and MIPI CSI-2.
Sources: SKU-7 Architecture Guide, "Architecture Overview" and "Key Data Flows"; diagram spec scripts/sku-diagrams/specs.py (sku7); product page record (sku7) blocks and blockNote; Technical Annex v3, sheet 8.

## Slide 5
04 · COMPONENTS
Four block groups turn one chirp into targets
The product specification's four block groups: two on the SiGe die, two on the CMOS die.
DEEPGRID SEMI · SKU-7 77 GHZ MIMO RADAR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
05
SiGe die: transmit
Makes a chirp that sweeps 4 GHz on a linear, low-noise ramp.
40 MHz crystal and ramp generator (sawtooth or triangle); fractional-N PLL with 1 MHz loop bandwidth; 38.5 GHz SiGe HBT VCO; doubler to 77 GHz; two 13 dBm power amplifiers.
SiGe die: receive
Turns four echoes into IF: beat frequency carries range, phase across receivers carries angle.
Four identical channels, each an LNA at 3.5 dB noise figure, a mixer fed by the LO from the doubler, an IF amplifier and a 10 MHz anti-alias filter.
CMOS die: digitise
Samples the four IF signals across the package boundary from the RF.
Four 12-bit 40 MSPS converters, one per receive channel, followed by Hann or Blackman windowing ahead of the range FFT.
CMOS die: detect
Turns the samples into a list of tracked targets.
1024-point radix-4 range FFT at 26 µs per chirp; 128-point Doppler FFT; 512 KB range-Doppler memory; cell-averaging CFAR; digital-beamforming angle estimation at 15°; tracker for up to 64 targets.
Package boundary: only the four IF signals cross from the receive group to the digitise group.
Source: product specification (SKU-7), block groups; SKU-7 Architecture Guide, component sections. Pre-silicon design targets.
Notes: Four block groups, following the product specification.
Transmit, on the SiGe die: 40 MHz crystal, a ramp generator for sawtooth or triangle chirps, a fractional-N PLL with 1 MHz loop bandwidth, a 38.5 GHz SiGe HBT VCO, a doubler to 77 GHz and two 13 dBm power amplifiers. The guide's reason: a 4 GHz sweep gives 3.75 cm range resolution, and only a SiGe HBT reaches 77 GHz on a mature node.
Receive, on the SiGe die: four identical channels of LNA at 3.5 dB noise figure, mixer fed by the LO, IF amplifier and 10 MHz anti-alias filter. The beat frequency carries range; the phase across the four receivers carries the angle of arrival.
Digitise, on the CMOS die: four 12-bit 40 MSPS converters and Hann or Blackman windowing. "One per receive channel" is our reading of four converters for four channels.
Detect, on the CMOS die: 1024-point radix-4 range FFT at 26 µs per chirp, 128-point Doppler FFT, 512 KB range-Doppler memory, cell-averaging CFAR, digital-beamforming angle estimation at 15° resolution, and a tracker for up to 64 targets per frame.
Sources: product page record (sku7) blocks; SKU-7 Architecture Guide, "Component" sections.

## Slide 6
05 · DESIGN DECISIONS
Two dies buy RF margin and add a boundary
Four architecture choices, what each one buys, and what each asks of the design.
DEEPGRID SEMI · SKU-7 77 GHZ MIMO RADAR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
06
DECISION
WHAT IT BUYS
WHAT IT COSTS
SiGe HBT front end on IHP SG13G2
Transistors with fT above 350 GHz give gain at 77 GHz that standard CMOS lacks.
No FPGA equivalent: the front end is proven on silicon or not at all, across IHP wafer runs.
38.5 GHz VCO, doubler and fractional-N PLL
A 4 GHz sweep in the 76 to 81 GHz band, for 3.75 cm range resolution.
The ramp must stay linear across 4 GHz; the open target is under 50 kHz rms error without ghost targets.
Converters and FFTs on a separate CMOS die
Fast sampling and 1024-point FFTs run away from the sensitive receivers.
Four IF signals cross a package boundary and need clean substrate transmission lines.
Two transmit, four receive, digital beamforming
Angle of arrival from the phase across four receivers, computed on the CMOS die.
Four receivers set the angle-resolution target at 15°.
Probe first
The die boundary and the chirp ramp. Both are open questions the design team has set itself (slide 9).
Retired only on silicon
The SiGe front end has no FPGA stand-in, so its targets stay targets until the IHP wafer run.
Source: product specification (SKU-7), physics, specs and questions; Technical Annex v3, sheet 8. Costs follow from the named mechanism.
Notes: Every choice buys capability and asks something of the design; the costs are what to probe in evaluation.
Process: SiGe heterojunction transistors on IHP SG13G2 with fT above 350 GHz give the gain margin at 77 GHz. The cost is printed on the annex sheet itself: the SiGe front end has no FPGA equivalent and is proven on silicon or not at all, so risk comes down only across IHP wafer runs.
Chirp: a 38.5 GHz VCO behind a fractional-N PLL, doubled to 77 GHz, sweeps 4 GHz for 3.75 cm range resolution. The ramp has to stay linear; the design's own open target is under 50 kHz rms error across the sweep without ghost targets.
Partition: converters and FFTs sit on a separate 130 nm CMOS die, away from the receivers. The cost is the boundary itself: four IF signals cross the package, which needs clean substrate transmission lines.
Array: two transmitters and four receivers with digital beamforming; angle resolution targets 15° from four receivers.
The "what it costs" column is a fair reading of each named mechanism and of the product specification's own questions, not a measured penalty.
Sources: product page record (sku7) physics, specs and questions; Technical Annex v3, sheet 8 ("Honesty on the sheet").

## Slide 7
06 · KEY DATA FLOW
Six steps take a chirp to a tracked target
Steps 1 to 3 run on the SiGe die; step 4 is the only die crossing; steps 5 and 6 run on CMOS.
DEEPGRID SEMI · SKU-7 77 GHZ MIMO RADAR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
07
SIGE DIE
CMOS DIE
1
Synthesise
The crystal, ramp generator, PLL and VCO synthesise the chirp.
2
Transmit
The doubler reaches 77 GHz and the two PAs transmit.
3
Receive
Each of four echoes is amplified, mixed with the LO and filtered.
4
Cross
The IF signals cross to the CMOS die, are digitised at 12 bits and feed the range FFT.
5
Detect
The range-Doppler map feeds CFAR detection and angle estimation.
6
Report
The target list goes to the ECU over CAN-FD, 100BASE-T1 or MIPI CSI-2.
What crosses the die boundary
Only the four IF signals. Everything at 77 GHz stays on the SiGe die; sampling and every FFT run on the 130 nm CMOS die at 200 MHz.
What leaves the radar
A target list of range, velocity, angle and RCS for up to 64 tracks per frame, over CAN-FD, 100BASE-T1 or MIPI CSI-2.
Source: SKU-7 Architecture Guide, "Key Data Flows" 1 to 6; product specification block note (IF crosses, converters on CMOS).
Notes: Walk the six steps. 1: the crystal, ramp generator, PLL and VCO synthesise the chirp. 2: the doubler reaches 77 GHz and the two PAs transmit. 3: each of four echoes is amplified, mixed with the LO and filtered. 4: the IF signals cross to the CMOS die, are digitised at 12 bits, 40 MSPS, and feed the 1024-point range FFT. 5: the range-Doppler map feeds CFAR detection and angle estimation. 6: the target list goes to the ECU.
Step 4 is the one to dwell on: it is the only place the signal leaves one die for the other, and it is the first of the four evaluator questions.
Reconciliation: the guide's step 3 ends "and digitised" and its step 4 says "the 12-bit samples cross"; the product specification places the converters on the CMOS die and has the IF cross the boundary, and this deck follows it.
Sources: SKU-7 Architecture Guide, "Key Data Flows"; product page record (sku7) blockNote and specs; Technical Annex v3, sheet 8.

## Slide 8
07 · ARCHITECTURE TARGETS
Every figure here is a target, not a measurement
Architecture targets from the product specification. No SKU-7 silicon has been built or measured.
DEEPGRID SEMI · SKU-7 77 GHZ MIMO RADAR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
08
PARAMETER
ARCHITECTURE TARGET
STATUS
RF process
130 nm SiGe BiCMOS (IHP SG13G2), fT above 350 GHz
TARGET
Baseband process
130 nm CMOS at 200 MHz
TARGET
Array
Two transmit, four receive (MIMO)
TARGET
Sweep
4 GHz in the 76 to 81 GHz band; 3.75 cm range resolution
TARGET
Conversion
Four 12-bit 40 MSPS ADCs
TARGET
Processing
Range and Doppler FFT, CFAR, angle estimation, 64-target tracker
TARGET
Interfaces
CAN-FD, 100BASE-T1, MIPI CSI-2
TARGET
Designed toward, not certificates held: ISO 26262 ASIL-B · DO-160G · MIL-STD-883K
Source: product specification (SKU-7), specs and designed-toward list. Status: pre-silicon; IHP wafer run planned FY28.
Notes: Every row is an architecture target from the product specification. None is a datasheet value and none is measured: SKU-7 has no silicon yet, and the SiGe front end cannot be stood in for on an FPGA. Status: IHP wafer run, FY28.
Standards appear only as design direction. ISO 26262 ASIL-B, DO-160G and MIL-STD-883K are targets the design is developed toward; no certificate exists for any DeepGrid part.
Guide-level detail behind these rows, also targets: 40 MHz crystal, 1 MHz PLL loop bandwidth, 38.5 GHz VCO, 13 dBm per PA, 3.5 dB LNA noise figure, 10 MHz anti-alias filter, 26 µs range FFT per chirp, 128-point Doppler FFT, 512 KB map memory, 15° angle resolution, up to 64 tracks per frame.
Sources: product page record (sku7) specs and designedToward; SKU-7 Architecture Guide, component sections and "Designed toward"; applications status record (sku7).

## Slide 9
08 · QUESTIONS AN EVALUATOR SHOULD ASK
Four questions decide if it fits your platform
The design team's own open questions. Each needs data before a design-in decision.
DEEPGRID SEMI · SKU-7 77 GHZ MIMO RADAR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
09
1
The die boundary
What substrate transmission lines keep the IF signal clean between the SiGe and CMOS dies?
2
Chirp linearity
Can the ramp hold under 50 kHz rms error across 4 GHz without ghost targets?
3
Silicon risk
With no FPGA stand-in for the front end, how is risk reduced across IHP wafer runs?
4
Co-existence
On a mast beside UHF and VHF radios, what shielding keeps local-oscillator harmonics out of them?
Source: product specification (SKU-7), engineering questions. Pre-silicon: no answer here is a measured result yet.
Notes: These four questions come from the design itself; they are what an evaluator should ask the team to answer with data.
1. The die boundary: what substrate transmission lines keep the IF signal clean between the SiGe and CMOS dies?
2. Chirp linearity: can the ramp hold under 50 kHz rms error across 4 GHz without ghost targets?
3. Silicon risk: with no FPGA stand-in for the front end, how is risk reduced across IHP wafer runs?
4. Co-existence: on a mast beside UHF and VHF radios, what shielding keeps local-oscillator harmonics out of them?
Pre-silicon, none of these has a measured answer yet; that is exactly why they belong in the evaluation.
Sources: product page record (sku7) questions.

## Slide 10
09 · SUMMARY AND NEXT STEP
Test the targets before the IHP wafer run
SKU-7 is an architecture with stated targets; your platform needs are the fastest way to test it.
DEEPGRID SEMI · SKU-7 77 GHZ MIMO RADAR · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
10
WHAT TO TAKE AWAY
Two dies: a SiGe front end on IHP SG13G2 for 77 GHz, and a 130 nm CMOS die for conversion, FFTs, detection and tracking.
Targets: 4 GHz sweep for 3.75 cm range resolution, two transmit and four receive channels, up to 64 tracked targets.
Pre-silicon: IHP wafer run planned FY28. The front end has no FPGA stand-in; nothing is measured yet.
1
Share your platform
Mounting, range and angle needs, nearby radios, and the ECU interface your unit uses.
2
Put the four questions
Die boundary, chirp linearity, silicon risk and co-existence, answered with the design team.
3
Scope an evaluation
Check the architecture targets against your platform and agree what the first wafer run must show.
NEXT STEP · EVALUATION PATH
Start an evaluation: group@deepgrid.in · send your platform and interface needs
Notes: Close on the action. SKU-7 splits a 77 GHz radar across two dies: a SiGe front end for the chirp, two transmitters and four receive channels, and a 130 nm CMOS die that digitises, transforms, detects and tracks. All figures are architecture targets; the part is pre-silicon, with an IHP wafer run planned for FY28, and the front end can only be proven on silicon.
The ask: send your platform needs (mounting, range and angle requirements, nearby radios, ECU interface) to group@deepgrid.in. The evaluation starts by checking the slide 8 targets against your platform and putting the four questions from slide 9 to the design team.
Sources: product page record (sku7); applications status record (sku7); company contact page (group@deepgrid.in).