## Slide 1
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER AND TCON · SYSTEM ARCHITECTURE
A display driver that notices
a frozen picture
A timing controller and a 1280-channel, 10-bit source driver on one 130 nm high-voltage die.
1280 × 10-bit
COLUMN DACS
Precharge: about 40% less drive power
0 to 12 V
COLUMN SWING
Plus a 24 V gate level shift for the rows
2 frames
FREEZE ALERT
Frame-by-frame CRC comparison in hardware
STATUS
Pre-silicon. Every figure in this deck is an architecture target, not a measurement. Evidence today is the architecture sheet; the die is planned for the Cycle-3 wafer run.
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
01
Notes: SKU-8 is a rugged display driver: a timing controller and a 1280-channel, 10-bit source driver on one 130 nm high-voltage die.
Headline: product page SKU-8, headline ("A cockpit display driver that notices when the picture freezes") and lede.
Figures: product page specs (Column outputs: 1280 × 10-bit DACs with charge-sharing precharge, about 40% less drive power; Output swing: 0 to 12 V, 24 V gate level shift; Safety: frame-freeze self-test, alert within two frames) and physics 3 (frame-by-frame CRC comparison in hardware).
Status: the site's applications record for SKU-8 (status "Cycle-3 wafer run"; evidence "Architecture sheet").
Say plainly: pre-silicon. Every value is a design target (architecture guide, scope note).

## Slide 2
Timing, pixels and 12 V drive on one die
A timing controller, a temperature-compensated pixel pipeline and a high-voltage column and row driver.
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
02
01 · WHAT IT IS
Timing controller
Takes video over dual LVDS, four-lane MIPI DSI or parallel RGB into a four-line buffer, sets programmable timing from a 100 MHz PLL and checks every frame for a freeze.
TCON · PLL · BIST + safety
Pixel pipeline
De-gamma, a 3 × 3 colour matrix with white point, a 14-bit gamma table with temperature feedback, and temporal and spatial dither, ready for the column DACs.
De-gamma · Colour · Gamma · Dither
High-voltage drive
1280 10-bit DAC channels and 0 to 12 V output amplifiers with charge-sharing precharge, plus a 24 V gate-driver level shift, VCOM and backlight control.
Columns 0 to 12 V · Rows 24 V
WHAT IT REPLACES
Imported display timing controllers and source drivers, in cockpit, vehicle instrument, industrial control and rail passenger displays.
WHAT SKU-8 IS BUILT ON
One 130 nm high-voltage die: timing and pixel logic beside thick-oxide amplifiers that reach 12 V on the columns and 24 V on the rows.
Evidence today: the architecture sheet. Pre-silicon; no figure in this deck is a silicon measurement.
Notes: Three jobs, one die.
Cards: product page SKU-8, blocks (Video input; Pixel pipeline; Timing and safety; Column drive; Row and backlight) and specs (Inputs; Gamma; Output swing). Detail: architecture guide, Architecture Overview items 1 to 5 (3 × 3 colour matrix with white point; temporal and spatial dithering).
"What it replaces": the site's applications record for SKU-8 ("Imported display timing controllers and source drivers"); the display types are the record's roles for SKU-8 (rugged cockpit displays; industrial control panels, rail passenger displays and automotive instrument clusters).
Related parts on the product page: SKU-3 generates the display bias rails; SKU-9 handles the graphics stream in a vehicle.

## Slide 3
Three panel requirements dictate the silicon
The requirement on the left, the consequence in silicon in the middle, and the blocks that carry it.
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
03
02 · WHY ITS OWN SILICON
THE PANEL REQUIRES
SO THE SILICON NEEDS
WHERE IT LANDS
Panel columns swing 0 to 12 V and row drivers need 24 V.
Thick-oxide high-voltage amplifiers and level shifters on a 130 nm HV process; dense nodes cannot reach these voltages.
Column drive + row
Output amps 0 to 12 V · gate level shift 24 V
Contrast must hold at +85 °C in direct sun.
An on-die temperature sensor feeding a 14-bit gamma table.
Pixel pipeline
Gamma table 14-bit · temperature feedback
A frozen display in a cockpit is a hazard, not a glitch.
Frame-by-frame CRC comparison in hardware.
Timing + safety
Frame-freeze self-test · alert within two frames
A 0 to 12 V swing on thick oxide is mature-node territory; precharge cuts driver power by about 40%.
Notes: The panel physics forces the architecture.
Requirement and consequence rows: product page SKU-8, physics (all three pairs, verbatim).
"Where it lands": product page blocks (Column drive; Row and backlight; Pixel pipeline; Timing and safety) and specs (Safety: alert within two frames).
Closing line: architecture guide, Component: Column (source) drivers, "Why it exists".

## Slide 4
One frame crosses five zones to reach the panel
Video input, pixel pipeline and timing on a control bus, driving high-voltage columns and the rows.
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
04
03 · SYSTEM ARCHITECTURE
LVDS · MIPI DSI · PARALLEL RGB
VIDEO INPUT
PIXEL PIPELINE
TIMING + TEST
LVDS RX
dual, 655 Mbps/lane
DSI RX
MIPI · four lanes
Line buffer
dual-port SRAM · 4 lines × 1280 × 24 bit
De-gamma
input linearise
Colour
3 × 3 colour matrix
Dither
temporal + spatial
Gamma table
14-bit · temp feedback
TCON
H/V timing, porches
PLL
100 MHz
Test pattern
colour bars
BIST + safety
frame-freeze check
CONTROL BUS · SPI / I²C REGISTER FILE
COLUMN (SOURCE) DRIVERS · HIGH-VOLTAGE
ROW + BACKLIGHT
DAC bank
1280 × 10-bit · resistor string + buffer
Output amps
rail-to-rail HV · 0 to 12 V · thick oxide
Column outputs × 1280
3 sub-pixels each → 3,840 outputs · charge-sharing precharge
Gate driver IF
row scan, 24 V shift
VCOM
common electrode
Backlight
PWM LED · 8 dimming zones
Ambient
light + temperature
1
2
3
4
5
TO THE PANEL · SOURCE / GATE / VCOM / LED
1
Video arrives over LVDS, DSI or parallel RGB.
2
The line buffer feeds the pipeline, 24 bits a pixel.
3
Dithered pixels drive the column DACs.
4
HV amplifiers drive the 3,840 column outputs.
5
The TCON scans rows through the gate driver.
Notes: Read the markers 1 to 5: video in, through the line buffer into the pixel pipeline, dithered pixels into the column DACs, the high-voltage amplifiers onto the column outputs, and the timing controller scanning the rows.
Structure: redrawn from the Technical Annex v3, sheet 9, through the site's diagram spec for SKU-8 (zones, blocks, edges and markers); the column-driver zone keeps the sheet's layout (DAC bank over output amps, column outputs to the right).
Values follow the product page SKU-8 (blocks, specs, physics): dual LVDS at 655 Mbps per lane, four-lane MIPI DSI, a 100 MHz PLL, a 14-bit gamma table with temperature feedback, alert within two frames. The annex sheet draws a 10-bit-per-channel gamma LUT; the product page's 14-bit table is used (architecture guide, "Where this differs from the annex sheet").
Block detail not on the product page comes from the architecture guide, Components (line buffer 4 lines × 1280 × 24 bit; 3 × 3 matrix with white point; resistor-string DAC; 3 sub-pixels × 1280 = 3,840 outputs; 8 local-dimming zones). The sources give 1280 DACs and 3,840 sub-pixel outputs; how DACs map to sub-pixels is not stated.
The control-bus clock printed on the sheet is not drawn: the product page gives none. Every value is a design target.

## Slide 5
Four block groups, each answering one requirement
What each group does and why it is there, with the blocks that carry it.
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
05
04 · INSIDE THE PART
BLOCK GROUP 1
Video input + pixel pipeline
Dual LVDS at 655 Mbps per lane, four-lane MIPI DSI or parallel RGB fill a four-line buffer. De-gamma, colour matrix, 14-bit gamma and dither follow. Why: LCD response shifts with panel temperature.
LVDS RX · DSI RX · Line buffer · Gamma table
BLOCK GROUP 2
Timing and safety
A programmable timing controller with a 100 MHz PLL sets the porches; a colour-bar pattern supports test. The self-test compares frame CRCs. Why: a frozen cockpit display is a hazard.
TCON · PLL · Test pattern · BIST + safety
BLOCK GROUP 3
Column drive, high-voltage
1280 10-bit resistor-string DACs feed rail-to-rail amplifiers swinging 0 to 12 V on thick oxide. Charge-sharing precharge between columns cuts drive power by about 40%.
DAC bank · Output amps · Column outputs
BLOCK GROUP 4
Row and backlight
A 24 V level shift drives the gate-driver row scan. A VCOM generator sets the common electrode; the PWM LED backlight has eight local-dimming zones and an ambient light input.
Gate driver IF · VCOM · Backlight · Ambient
Notes: Four block groups, one job each.
Text: product page SKU-8, blocks (Video input; Pixel pipeline; Timing and safety; Column drive; Row and backlight) and physics (the "Why" lines).
Block detail: SKU-8 architecture guide, Components (Pixel pipeline "Why it exists": LCD response shifts with panel temperature; Timing + test: programmable porches, colour bars; Column drivers: resistor-string DAC, rail-to-rail HV amps, thick oxide, about 40%; Row + backlight: local dimming, 8 zones).
All values are architecture targets from the Technical Annex v3, sheet 9, as carried by the product page.

## Slide 6
Four decisions, and the question that tests each
Each choice, the alternative it rules out, the reason, and the check an evaluator should run.
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
06
05 · DESIGN DECISIONS
DECISION
INSTEAD OF
WHY
WHAT TO VERIFY
130 nm high-voltage CMOS for the whole die
A dense digital node
Columns swing 0 to 12 V and rows need 24 V; dense nodes cannot reach these voltages.
Which voltages force the high-voltage process.
Charge-sharing precharge between adjacent columns
Driving every column from the rail
Precharge cuts driver power by about 40%.
How much energy precharge recovers during full-screen video.
A 14-bit gamma table with temperature feedback
A fixed gamma curve
Contrast must hold at +85 °C in direct sun, and LCD response shifts with panel temperature.
How the table tracks temperature to hold contrast at +85 °C.
Frame-by-frame CRC comparison in hardware
Leaving freeze detection to host software
A frozen cockpit display is a hazard; the alert must come within two frames.
How successive frame CRCs raise the alert within two frames.
Each row maps to one of the four evaluator questions on slide 9.
Notes: Four decisions, each with a check.
Row 1: product page physics 1 and specs (Process; Output swing); question "Why 130 nm".
Row 2: product page specs (Column outputs: about 40% less drive power); architecture guide, Column drivers "Why it exists"; question "Charge sharing".
Row 3: product page physics 2 and specs (Gamma); guide, Pixel pipeline "Why it exists"; question "Heat and contrast".
Row 4: product page physics 3 and specs (Safety); question "Freeze detection".
The "Instead of" column names the alternative each decision rules out; it is a reading of the sources, not a measured comparison.

## Slide 7
Five steps take a frame from input to the panel
The frame path, numbered as on the diagram, and the two checks that run beside it.
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
07
06 · KEY DATA FLOW
1
Receive
Video arrives over dual LVDS, four-lane MIPI DSI or parallel RGB.
2
Buffer
The four-line buffer feeds the pixel pipeline, 24 bits per pixel.
3
Convert
Dithered pixels drive the 1280 10-bit column DACs.
4
Drive
High-voltage amplifiers swing the 3,840 column outputs, 0 to 12 V.
5
Scan
The timing controller scans the rows through the 24 V gate driver.
The freeze check runs beside the pixel path
The self-test compares a CRC of every frame with the next in hardware. If the image stops updating, it raises an alert within two frames, without waiting on host software.
BIST + safety · alert within two frames
Temperature closes the gamma loop
An on-die temperature sensor feeds the 14-bit gamma table, so the curve follows panel temperature and contrast holds at +85 °C in direct sun.
Ambient sense · Gamma table · Dither
Notes: One frame, five steps; then the two loops beside the path.
Steps 1 to 5: SKU-8 architecture guide, Key Data Flows; the same markers as the system diagram (diagram spec for SKU-8, markers). Step detail: product page blocks and specs (Inputs; Column outputs; Output swing).
Freeze card: product page physics 3 (frame-by-frame CRC comparison in hardware), specs (alert within two frames) and the question "Freeze detection". "Without waiting on host software" is a reading of "in hardware".
Temperature card: product page physics 2 (on-die temperature sensor feeding a 14-bit gamma table; contrast at +85 °C in direct sun); guide, Pixel pipeline (temperature feedback) and Row + backlight (Ambient: light + temp sense).

## Slide 8
Every figure here is a target, not a measurement
Seven rows from the product page specification, each labelled a target, and where the annex differs.
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
08
07 · ARCHITECTURE TARGETS
PARAMETER
ARCHITECTURE TARGET
STATUS
Process
130 nm high-voltage CMOS
Target
Resolution
SXGA 1280 × 1024 at 60 Hz; WXGA and Full HD variants
Target
Column outputs
1280 × 10-bit DACs with charge-sharing precharge (about 40% less drive power)
Target
Output swing
0 to 12 V; 24 V gate level shift
Target
Inputs
Dual LVDS, MIPI DSI, parallel RGB
Target
Gamma
14-bit table with temperature feedback
Target
Safety
Frame-freeze self-test, alert within two frames
Target
Designed toward
ISO 26262 ASIL-B; MIL-STD-810G; DEF-STAN 00-35. Targets the design is developed toward, not certificates held.
Follows the product page
Annex sheet 9 draws a 10-bit-per-channel gamma LUT, two-lane DSI and a 108 MHz pixel clock. This deck uses the product page: a 14-bit table, four-lane DSI, a 100 MHz PLL.
Evidence today
Pre-silicon. The architecture sheet; the die is planned for the Cycle-3 wafer run.
Notes: Targets, not measurements.
Table: product page SKU-8, specs (all seven rows, verbatim values).
Designed toward: product page designedToward; architecture guide, Designed toward and scope note ("no certificate exists for any DeepGrid part").
Follows the product page: the product page is the value authority. The guide records the gamma difference ("10-bit per channel on the sheet, a 14-bit table here"); the two-lane DSI and 108 MHz pixel clock are the sheet's and guide's values, which the product page replaces with four-lane MIPI DSI and a 100 MHz PLL.
Evidence today: the site's applications record for SKU-8 (status "Cycle-3 wafer run"; evidence "Architecture sheet").

## Slide 9
Four questions decide whether SKU-8 fits your panel
Put these to DeepGrid before committing bench time. Each tests one part of the architecture.
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
09
08 · EVALUATOR QUESTIONS
Why 130 nm
Which voltages force the driver onto a high-voltage process rather than a dense digital one?
Tests the output amps and the 24 V gate level shift
1
Charge sharing
How much energy does precharge between adjacent columns recover during full-screen video?
Tests the column outputs and their precharge
2
Freeze detection
How do successive frame CRCs alert the operator within two frames if the image stops updating?
Tests the BIST + safety block
3
Heat and contrast
How does the gamma table track temperature to hold contrast at +85 °C?
Tests the gamma table and the temperature sense
4
The architecture sheet asks these of itself. Each needs silicon, a test chip or a dated plan to settle.
Notes: Four questions, verbatim from the product page SKU-8, questions (titles and wording unchanged).
The "Tests" line maps each question to the blocks on slides 4 and 5 that must answer it.
"Each needs silicon, a test chip or a dated plan to settle" follows from the pre-silicon status (architecture guide scope note).

## Slide 10
09 · NEXT STEP
Test it against your panel, sunlight and safety case
Bring three things to the first call: your panel resolution and column and row voltages, your temperature and sunlight envelope, and the freeze-alert time your safety case needs.
DISCUSS THIS PART
group@deepgrid.in
Subject: SKU-8 rugged display driver
WHAT TO TAKE AWAY
Drives
1280 10-bit columns at 0 to 12 V and the rows through a 24 V level shift, on one 130 nm HV die.
Corrects
A 14-bit gamma table with temperature feedback, to hold contrast at +85 °C in direct sun.
Checks
Frame-by-frame CRC comparison in hardware flags a frozen picture within two frames.
Status
Pre-silicon, planned for the Cycle-3 wafer run. Every figure is an architecture target.
DEEPGRID SEMI · SKU-8 RUGGED DISPLAY DRIVER · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
10
Notes: One action: evaluate SKU-8 against the panel's voltages, the temperature and sunlight envelope, and the freeze-alert time the safety case needs.
Contact: the site's contact page addresses group@deepgrid.in; the product page "Discuss this part" action carries the part name.
Summary lines: product page SKU-8 (physics, blocks, specs, designedToward); status: the site's applications record for SKU-8.
Do not imply a datasheet, a certificate or a delivery date; none exists.