## Slide 1
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · SYSTEM ARCHITECTURE
The zonal edge of the vehicle,
not its computer
Vehicle networks in, switched power out: one 130 nm CMOS and BCD chip per zone of a software-defined vehicle.
16
SMART ELECTRONIC FUSES
Programmable trip and I²t; 12 V and 48 V
2-cycle
LOCKSTEP SAFETY ISLAND
ASIL-D as a design target, not a certificate
130 nm
CMOS AND BCD AT 200 MHZ
Central sub-10 nm compute not claimed
STATUS
Pre-silicon. Every figure in this deck is an architecture target, not a measurement. Evidence today is the architecture sheet; no certificate exists for any DeepGrid part.
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
01
Notes: SKU-9 is the zonal edge of a software-defined vehicle: it bridges in-vehicle networks to the local loads of one zone. The central multi-gigahertz computer is a sub-10 nm part and is not claimed.
Headline and subline: product page SKU-9, headline and lede; specs (Process: 130 nm CMOS and BCD at 200 MHz; Scope: zonal edge only).
Figures: product page specs (Power: 16 smart electronic fuses with programmable trip and I²t; Safety island: dual-core two-cycle lockstep) and physics (12 V and 48 V loads).
ASIL-D: the annex sheet 10 labels the island "ASIL-D certified"; the product page reconcile note states it as a design target, and no certificate exists for any DeepGrid part (architecture guide, scope note).
Status: the site's applications record for SKU-9 (evidence "Architecture sheet"). Say plainly: pre-silicon.

## Slide 2
One chip turns vehicle messages into switched power
Messages arrive on Ethernet, CAN and LIN, are scheduled and routed in hardware, and drive local loads.
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
02
01 · WHAT IT IS
Gateway in
Two 100BASE-T1, eight CAN-FD, one CAN-XL, eight LIN masters and one FlexRay. The gateway routes and rate-limits between domains.
Ethernet · CAN · LIN · FlexRay
Schedule and guard
A TSN switch schedules traffic against precision time. A two-cycle lockstep safety island and a hardware security module sit across every path.
802.1Qbv · 802.1AS · lockstep · HSM
Power out
Sixteen smart electronic fuses with programmable trip and I²t, eight high-side drivers and twelve PWM outputs drive the zone’s 12 V and 48 V loads.
Smart fuse × 16 · HS × 8 · PWM × 12
WHAT IT REPLACES
Relay boxes and point-to-point wiring harnesses, one wire per function.
WHERE THE LINE FALLS
130 nm at 200 MHz owns the zonal layer: gateway, smart I/O, safety and security edge. Central compute is a sub-10 nm part and is not claimed.
Evidence today: the architecture sheet. Pre-silicon; no figure in this deck is a silicon measurement.
Notes: One chip per zone: messages in, switched power out.
Cards: product page SKU-9, blocks (Vehicle networks; Real-time network; Safety island; Security; Zonal power) and blockNote. "Routes and rate-limits between domains" and "LIN masters": architecture guide, Component: In-vehicle network · gateway.
Port counts follow the product page: two 100BASE-T1, eight CAN-FD, one CAN-XL, eight LIN, one FlexRay. The annex sheet 10 draws CAN-XL × 2, FlexRay × 2 and a 1000BASE-T1 port; those are not claimed.
"What it replaces": the site's applications record for SKU-9 ("Relay boxes and point-to-point wiring harnesses"). "One wire per function" is a reading of point-to-point wiring.
"Where the line falls": the scope statement on annex sheet 10 as carried by the site's diagram spec (banner) and the product page lede.

## Slide 3
Three zone requirements dictate the silicon
The requirement on the left, its consequence in silicon in the middle, and the blocks that carry it.
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
03
02 · WHY ITS OWN SILICON
THE ZONE REQUIRES
SO THE SILICON NEEDS
WHERE IT LANDS
Switch and protect 12 V and 48 V loads in a harness.
BCD power devices for the smart fuses alongside the logic.
Zonal power + I/O
Smart fuse × 16 · HS driver × 8
Brake-by-wire messages need bounded latency on a shared link.
A time-aware shaper (802.1Qbv) and precision time sync (802.1AS) in hardware.
Real-time control
TSN switch · PTP sub-µs sync
Safety-critical and comfort functions share one chip.
A lockstep island with memory protection and bus firewalls for freedom from interference.
Safety island
Lockstep pair · comparator · MPU + bus firewall
None of the three needs multi-gigahertz compute; all three need power devices, timing and isolation in hardware.
Notes: The zone's physics forces the architecture.
Requirement and consequence rows: product page SKU-9, physics (all three pairs, verbatim).
"Where it lands": product page blocks (Zonal power; Real-time network; Safety island) and the architecture guide, Components (Smart fuse × 16, HS driver × 8; TSN switch, PTP 802.1AS clock, sub-µs sync; Comparator, Freedom from interference: MPU + bus firewall).
Closing line: a synthesis of the three rows and the product page lede (the central multi-gigahertz computer is a sub-10 nm part and is not claimed).

## Slide 4
Five zones on one crossbar; safety spans them all
Safety, security and real-time control above the crossbar; the network gateway and zonal power below.
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
04
03 · SYSTEM ARCHITECTURE
SAFETY ISLAND
DGridRiscV × 2
RV32IM_Zicsr · lockstep · 200 MHz · +2 cycle skew · PMP · ECC
Comparator
bus + retire · mismatch → safe state
Freedom from interference
MPU + bus firewall
SECURITY
HSM
AES-256 · ECC-256 · true RNG
Secure boot
root of trust · OTP key store · A/B slots
OTA engine
signed image verify + rollback
REAL-TIME CONTROL
TSN switch
802.1Qbv · time-aware shaper
PTP
802.1AS clock · sub-µs sync
Service router
SOME/IP + DoIP
On-chip crossbar · 200 MHz · 130 nm CMOS and BCD
IN-VEHICLE NETWORK · GATEWAY
100BASE-T1 × 2
automotive Ethernet
CAN-FD × 8
CAN-XL × 1
LIN × 8
masters
FlexRay × 1
ZONAL POWER + I/O
Smart fuse × 16
eFuse + sense · replaces relay box
HS driver × 8
load control
ADC 12-bit
24-ch sense
PWM × 12
actuator drive
To the zone harness · loads, sensors, actuators
1
2
3
4
5
1
Messages arrive on Ethernet, CAN and LIN.
2
The TSN switch schedules them against precision time.
3
The service router forwards them across the crossbar.
4
They become switched power at the smart fuses.
5
A lockstep mismatch drives the safe state.
Notes: Read the markers in order: 1 a message arrives at a gateway port (CAN-FD shown), 2 the TSN switch schedules it against PTP time, 3 the service router forwards it across the crossbar, 4 it becomes switched power at a smart fuse, 5 a lockstep mismatch at the comparator drives the safe state.
Structure: redrawn from the Technical Annex v3, sheet 10, through the site's diagram spec for SKU-9 (zones, blocks in their spec order, edges and markers).
Values: product page SKU-9 and the SKU-9 architecture guide (Architecture Overview; Components; Key Data Flows 1 to 5).
Network ports follow the product page: two 100BASE-T1, eight CAN-FD, one CAN-XL, eight LIN, one FlexRay. The annex sheet draws CAN-XL × 2, FlexRay × 2 and a 1000BASE-T1 port; they are not drawn here. The sheet's "ASIL-D" label on the safety island is not drawn; ASIL-D is a design target (product page reconcile).
Zone colours: red safety, purple security, blue real-time, green gateway, amber zonal power; cyan is the traced path. Every value is a design target.

## Slide 5
Safety, security, timing and power: one job each
What each block group does and why it is there, with the blocks that carry it.
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
05
04 · INSIDE THE PART
BLOCK GROUP 1
Safety island
Two DGridRiscV cores (RV32IM_Zicsr) run in lockstep with a two-cycle skew, PMP and ECC. A comparator on bus and retire sends any mismatch to the safe state. Why: safety and comfort share one chip.
DGridRiscV × 2 · Comparator · MPU + bus firewall
BLOCK GROUP 2
Security
A hardware security module with AES-256, ECC-256 and a true RNG. Secure boot starts from an OTP key store with A/B slots; the OTA engine verifies signed images and rolls back.
HSM · Secure boot · OTA engine
BLOCK GROUP 3
Real-time network
A TSN switch with an 802.1Qbv time-aware shaper and 802.1AS clock sync, a SOME/IP and DoIP service router, and the gateway ports. Why: brake-by-wire needs bounded latency.
TSN switch · PTP · Service router · ports
BLOCK GROUP 4
Zonal power + I/O
Sixteen smart fuses with sensing and programmable I²t trip replace the relay box, beside eight high-side drivers, twelve PWM outputs and a 24-channel 12-bit sense ADC. Why: 12 V and 48 V loads need BCD devices.
Smart fuse × 16 · HS × 8 · PWM × 12 · ADC
Notes: Four block groups, one job each. The real-time network group joins the guide's Real-time control zone and the gateway ports, as the product page blocks do.
Text: product page SKU-9, blocks (Safety island; Security; Real-time network; Vehicle networks; Zonal power) and physics (the "Why" lines).
Block detail: SKU-9 architecture guide, Components: Safety island (RV32IM_Zicsr, +2 cycle skew, PMP, ECC; comparator on bus and retire, mismatch to safe state), Security (OTP key store, A/B slots; signed image verify and rollback), Real-time control (802.1AS clock, SOME/IP and DoIP), Zonal power + I/O (eFuse and sense, replaces relay box; 24-channel sense ADC).
All values are architecture targets from the Technical Annex v3, sheet 10, as carried by the product page.

## Slide 6
Four decisions, and the check that tests each
Each choice, the alternative it rules out, the reason, and the check an evaluator should run.
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
06
05 · DESIGN DECISIONS
DECISION
INSTEAD OF
WHY
WHAT TO VERIFY
The zonal layer on 130 nm CMOS and BCD at 200 MHz
Folding the zone into the sub-10 nm central computer
Harness loads need BCD power devices beside the logic; the zone needs no multi-gigahertz compute.
Why the node line falls at the zone, and what stays with the central computer.
A time-aware shaper and precision time in hardware
Best-effort switching
Brake-by-wire messages need bounded latency on a link shared with bulk data.
Whether the shaper holds under 10 µs for brake-by-wire with bulk data on the port.
Solid-state smart fuses with programmable trip and I²t
A relay box
Sixteen fuses with sensing switch and protect 12 V and 48 V loads in the harness.
How a fuse cuts off in microseconds without avalanche damage from harness inductance.
A lockstep island behind an MPU and bus firewall
Separate chips for safety and comfort
Safety-critical and comfort functions share one chip, so interference is blocked in hardware.
Which rules keep lighting commands away from steering registers.
Each "What to verify" cell is one of the four evaluator questions on slide 9.
Notes: Four decisions, each with a check.
Row 1: product page specs (Process; Scope), physics 1 and lede (sub-10 nm central computer not claimed); question "Where the node line falls".
Row 2: product page physics 2; question "Bounded latency". The 10 µs figure is the question's own wording, not a target the product page states.
Row 3: product page specs (Power: programmable trip and I²t), physics 1; guide (Smart fuse: replaces relay box); question "Solid-state fusing".
Row 4: product page physics 3 and blocks (Safety island); guide (MPU + bus firewall); question "Isolation".
The "Instead of" column names the alternative each decision rules out; it is a reading of the sources, not a measured comparison.

## Slide 7
Four steps take a message to a load; one guards it
The message path, numbered as on the diagram, with the safe state and the update path beside it.
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
07
06 · KEY DATA FLOW
1
Arrive
A message arrives at a gateway port: Ethernet, CAN or LIN.
2
Schedule
The TSN switch places it in a time-aware window against 802.1AS time.
3
Route
The SOME/IP and DoIP service router forwards it across the crossbar.
4
Switch
It becomes switched power at a smart fuse, high-side driver or PWM output.
5
Guard
A lockstep mismatch at the comparator drives the safe state.
Every path is guarded
The comparator checks both cores on bus and retire; a mismatch drives the safe state. The MPU and bus firewall keep comfort traffic out of the safety island.
Step 5 · Comparator, freedom from interference
Every update is checked
Secure boot starts from a root of trust in an OTP key store. The OTA engine verifies each signed image into the A/B slots and rolls back.
HSM · Secure boot · OTA engine
Notes: Four steps from a gateway port to a switched load; step 5 is the guard that runs alongside, not a fifth hop.
Steps 1 to 5: SKU-9 architecture guide, Key Data Flows; the same markers as the system diagram (diagram spec for SKU-9, markers). Step detail: product page blocks and blockNote; guide Components (Service router: SOME/IP + DoIP; PTP: 802.1AS).
Guard card: guide, Component: Safety island (comparator on bus and retire, mismatch to safe state; MPU + bus firewall); product page physics 3.
Update card: guide, Component: Security (root of trust, OTP key store, A/B slots; signed image verify + rollback); product page specs (Security: over-the-air update bank).
No latency, fault-reaction or update-time figure is stated: the annex sheet's characteristic charts are marked illustrative and are not on the product page.

## Slide 8
Every figure here is a target, not a measurement
Six rows from the product page specification, each labelled a target, with the annex differences.
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
08
07 · ARCHITECTURE TARGETS
PARAMETER
ARCHITECTURE TARGET
STATUS
Process
130 nm CMOS and BCD at 200 MHz
Target
Safety island
Dual-core two-cycle lockstep
Target
Security
Hardware security module, secure boot, over-the-air update bank
Target
Networking
TSN switch; 2 × 100BASE-T1, 8 × CAN-FD, CAN-XL, 8 × LIN, FlexRay
Target
Power
16 smart electronic fuses with programmable trip and I²t
Target
Scope
Zonal edge only; central compute is out of scope
Target
Designed toward
ISO 26262 ASIL-D; EVITA Full; AUTOSAR Classic 4.4; AEC-Q100 Grade 1. Targets the design is developed toward, not certificates.
Differs from the annex sheet
The sheet labels the island "ASIL-D certified" and draws CAN-XL × 2, FlexRay × 2 and a 1000BASE-T1 port. Here: ASIL-D as a target, one CAN-XL, one FlexRay, no 1000BASE-T1.
Evidence today
Pre-silicon. The architecture sheet; no certificate exists for any DeepGrid part.
Notes: Targets, not measurements.
Table: product page SKU-9, specs (all six rows, verbatim values). Networking reads one CAN-XL and one FlexRay.
Designed toward: product page designedToward; architecture guide, Designed toward and scope note ("no certificate exists for any DeepGrid part").
Differs from the annex sheet: product page reconcile ("ASIL-D certified" on the sheet is stated as a design target) and the architecture guide section "Where this differs from the annex sheet" (CAN-XL × 2, FlexRay × 2 and a 1000BASE-T1 port on the sheet).
Evidence today: the site's applications record for SKU-9 (evidence "Architecture sheet").

## Slide 9
Four questions decide whether SKU-9 fits your zone
Put these to DeepGrid before committing bench time. Each tests one part of the architecture.
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
09
08 · EVALUATOR QUESTIONS
Where the node line falls
Why does the zonal layer belong on 130 nm while central compute needs a sub-10 nm process?
Tests the process choice and the scope line
1
Bounded latency
Can the shaper guarantee under 10 µs for brake-by-wire traffic while bulk data shares the port?
Tests the TSN switch and PTP
2
Solid-state fusing
How do the smart fuses cut off in microseconds without avalanche damage from harness inductance?
Tests the smart fuses on 130 nm BCD
3
Isolation
Which memory-protection and firewall rules keep lighting commands away from steering registers?
Tests the MPU and bus firewall
4
The architecture sheet asks these of itself. Each needs silicon, a test chip or a dated plan to settle.
Notes: Four questions, verbatim from the product page SKU-9, questions (titles and wording unchanged).
The "Tests" line maps each question to the blocks on slides 4 and 5 that must answer it.
"Under 10 µs" is the question's figure, not a stated target. The annex sheet's illustrative gateway-latency chart is not used.
"Each needs silicon, a test chip or a dated plan to settle" follows from the pre-silicon status (architecture guide scope note).

## Slide 10
09 · NEXT STEP
Test it against your zone’s loads and latency
Bring four things to the first call: the zone, its loads and buses, the latency its messages need, and the safety target.
DISCUSS THIS PART
group@deepgrid.in
Subject: SKU-9 zonal controller and gateway
WHAT TO TAKE AWAY
Bridges
Two 100BASE-T1, eight CAN-FD, one CAN-XL, eight LIN and one FlexRay, routed between domains.
Schedules
A TSN switch with 802.1Qbv and 802.1AS in hardware, for bounded-latency brake-by-wire traffic.
Isolates
A two-cycle lockstep island, an MPU and bus firewall, and an HSM with secure boot and signed updates.
Switches
Sixteen smart fuses with programmable I²t trip, eight high-side drivers and twelve PWM outputs.
Status
Pre-silicon. Every figure is an architecture target; ASIL-D is a design target. Central compute is not claimed.
DEEPGRID SEMI · SKU-9 ZONAL CONTROLLER AND GATEWAY · ARCHITECTURE TARGETS, PRE-SILICON · OCTOBER 2026
10
Notes: One action: evaluate SKU-9 against the zone's loads, buses, latency and safety target.
The four things to bring: the site's vehicles area record ("The zone, its loads and buses, the latency the messages need and the safety target are what we need to answer").
Contact: the site's contact page addresses group@deepgrid.in.
Summary lines: product page SKU-9 (blocks, specs, physics, designedToward, reconcile); status: the site's applications record for SKU-9.
Do not imply a datasheet, a certificate or a delivery date; none exists.